## Slide 1: Internal Auditing and Control of Nonconforming Work
ISO/IEC 17025, clauses 4.14 and 4.9

## Slide 2: What will be covered in this training?
Internal Auditing
  What is it?
  Who performs it?
  What are the possible outcomes?
Control of Nonconforming Work
  What is it?
  How do I identify it?
  What do I do if it happens?

## Slide 3: Terms, Acronyms, and Definitions
Audit (assessment): The on-site verification activity, such as inspection or examination, of a process or quality system, to ensure compliance to requirements. An audit can apply to an entire organization or might be specific to a function, process or production step
Correction: The immediate fix to the problem
Corrective Action (CA): Need to dig deeper to find out “WHY”
Documents: “Say” what you are going to do
Nonconforming record (NCR): A permanent record—made in writing—for accounting and preserving the knowledge of a nonconforming condition for the purposes of documenting facts or events
Nonconformance: The nonfulfillment of a specified requirement or a failure to meet a professional standard

## Slide 4: Terms, Acronyms, and Definitions
Preventive Action: Action taken to remove or improve a process to prevent potential future occurrences of a nonconformance
Quality Audit: A systematic, independent examination and review to determine whether quality activities and related results comply with plans and whether these plans are implemented effectively and are suitable to achieve the objectives
Quality Management System (QMS): The quality, administrative and technical systems that govern the operations of the laboratory
Records: “Proof” of what you are doing
Root Cause: A factor that caused a nonconformance and should be permanently eliminated through process improvement

## Slide 5: Connections
How are internal audits and nonconforming work related to each other?
  Internal audits look for compliance with the ISO/IEC 17025 standard and quality management system. Noncompliance is also called nonconformance.
  Nonconformances can also be identified by ways other than internal audits.

## Slide 6: Internal Audit
  4.14.1 The laboratory shall periodically, and in accordance with a predetermined schedule and procedure, conduct internal audits of its activities to verify that its operations continue to comply with the requirements of the management system and this International Standard. The internal audit program shall address all elements of the management system, including the testing and/or calibration activities.
ISO/IEC 17025 clause 4.14

## Slide 7: ISO/IEC 17025:2005 Auditing Requirements
It is the responsibility of the quality manager to plan and organize audits as required by the schedule and requested by management. Such audits shall be carried out by trained and qualified personnel who are, wherever resources permit, independent of the activity to be audited.
  Note: The cycle for internal auditing should normally be completed in one year.

## Slide 8: ISO/IEC 17025:2005 Auditing Requirements
4.14.2 When audit findings cast doubt on the effectiveness of the operations or the correctness or validity of the laboratory’s test or calibration results, the laboratory shall take timely corrective action, and shall notify customers in writing if investigations show that the laboratory results may have been affected.

## Slide 9: ISO/IEC 17025:2005 Auditing Requirements
4.14.3 The area of activity audited, the audit findings and corrective actions that arise from them shall be recorded.
  4.14.4 Follow-up audit activities shall verify and record the implementation and effectiveness of the corrective action taken.

## Slide 10: Internal Auditors look for:
Does the laboratory “say” what they do?
  Do we have written documents (policies, procedures, arrangements) that meet the requirements of ISO/IEC 17025?
Does the laboratory “do” what we say?
  Are we in compliance with our own management system, the ISO/IEC 17025 standard, and our technical SOPs?
Can the laboratory “prove” it with records?
  Training records, standard preparation records, work books, customer reports, audit reports, are all examples of records (proof) that the laboratory is “doing what we say”.

## Slide 11: Purpose of Internal Audits:
Provide assurance to management that the quality management system is implemented as intended.
Identify opportunities for improving the management system itself and its effectiveness.
Find problems before they affect quality of data.
Prepare for external audits.
Can be used as training tool.
Internal auditing is a requirement of ISO/IEC 17025 Standard

## Slide 12: Basic Internal Audit Process
The audit schedule
The audit checklist
The auditors
Do
The audit as scheduled
Ask the questions
Examine the records
Check
Degree of conformity
Act
Cite nonconformities if non-compliances are found
Corrective Action/Closure
Plan
Usually planned by QA or QA Manager
Conducted by auditor, independent of area being audited
Does the laboratory meet requirements of ISO/IEC 17025 and its own SOPs
Findings include compliance, non-compliance, and opportunities for improvement

## Slide 13: Audit the System, NOT the People
Gather objective evidence
  Policies, SOPs, records, auditor observation
Interview the people
  Understand the system and its effectiveness
  How do they:
    Receive and interpret information
    Carry out instructions
    Produce the data
If nonconformances arise, fix that system
  Very few problems are due to the people
  The better the system, the fewer times people will be the problem

## Slide 14: Control of Nonconforming Work
  4.9.1 The laboratory shall have a policy and procedures that shall be implemented when any aspect of its testing work, or the results of this work, do not conform to its own procedures or the agreed requirements of the customers.
ISO/IEC 17025 clause 4.9

## Slide 15: Control of Nonconforming Work
  The policy and procedures:
    Establish responsibilities & authorities for managing nonconforming work
    Define actions taken when nonconforming work is identified (i.e. halting work, withholding reports)
    Ensure evaluation of significance of nonconforming work is made
    Ensure correction is taken immediately
    Determine if the nonconforming work is acceptable
    Ensure customer is notified if needed
    Define responsibility for authorizing resumption of work
ISO/IEC 17025 clause 4.9

## Slide 16: Control of Nonconforming Work
  4.9.2 Where the evaluation indicates that the nonconforming work could recur or that there is doubt about the compliance of the laboratory’s operations with its own policies and procedures, the corrective action procedure shall be promptly followed.
    4.9.1 (previous slide) required correction to always be taken when nonconforming work identified
    4.9.2 (this slide) only requires corrective action in certain circumstances
ISO/IEC 17025 clause 4.9

## Slide 17: What is nonconforming work?
Non-fulfillment of a requirement
When any aspect of testing or other work does not comply to procedures (our own or the customers’)
Out-of-control Quality Control
Incorrect results reported
Failing proficiency test
Requires evidence that a specific requirement was not met

## Slide 18: How a nonconformance is identified
Audit
Customer complaint/feedback
Quality control data
Proficiency test results
Observation/self-reporting

## Slide 19: How to respond to nonconforming work
Quality SOP (procedure) defines who can identify it and who is notified
Should work be halted?
Must data be withheld/reports recalled?
Evaluate the significance of the nonconformity
Correct it
Notify the customer, if needed
Resume work when appropriate

## Slide 20: Correction vs. Corrective Action
Correction
  An action to eliminate one instance of a nonconformity
  Does not identify causes
  Immediate fix
Corrective Action
  An action to identify and eliminate the cause of a nonconformity so that it will not happen again
  Prevent recurrence
  Problem solving process

## Slide 21: Correction Examples
Quality control (QC) samples fail:
  Correction: Re analyze the QC sample and all samples since the last QC was in control
Failure to complete all scheduled audits during the time period specified in quality management system
  Correction: Conduct the audits that were missed

## Slide 22: After the correction
Resume work and release data when appropriate and with proper authorization.
If deemed necessary, begin root cause analysis and corrective action process.
  Note: this is covered in a separate QMS Quick Learning Module

## Slide 23: Summing it up
Internal audits are planned activities, with the goal of assuring compliance to ISO/IEC 17025 and the laboratory’s policies and procedures.
A nonconformance requires immediate correction, along with additional decisions about significance of the nonconformity and acceptability of the work.

## Slide 24: Reference
ISO/IEC 17025:2005 General requirements for the competence of testing and calibration laboratories
–https://www.iso.org/standard/39883.html