## Slide 1: Root Cause Analysis & Corrective and Preventive Actions ISO/IEC 17025 Clauses 4.11 and 4.12

## Slide 2: What will be covered in this training?
Root Cause Analysis
  What it is
  Who performs it
  Sample methods for root cause analysis
Corrective Action & Preventive Action
  What is the difference between them
  When each applies

## Slide 3: Definitions
Continual Improvement: recurring activity to increase the ability to fulfill requirements
Correction: immediate action to elimate a detected nonconformity
Corrective Action: action to eliminate the cause of a detected nonconformity or other undesirable situation
Effectiveness: extent to which planned activities are realized and planned results achieved
Nonconformance: nonfulfillment of a requirement
Preventive Action: action to eliminate the cause of a potential nonconformance or other undesirable potential situation

## Slide 4: Root Cause Analysis
Root Cause Analysis/Investigation
  A type of problem solving method aimed at identifying the root cause(s) of a problem (nonconformance)
  The goal is to prevent recurrence of the nonconformance
  Is not a quick and easy process that can always be accomplished in an office or conference room
  Generally requires talking to the people involved who best know the process

## Slide 5: Root Cause Analysis
Takes place after the immediate correction of a nonconformance.
Required when a nonconformance is significant (could recur, casts doubt on a laboratory operation’s compliance with procedures)
Required for nonconformances identified through audits and for failing proficiency test reports.

## Slide 6: Laboratory SOP Must Define Authorities and Responsibilites
Responsibility and authority for the management of nonconformances
Actions to be taken when nonconforming work is identified
  This may include halting of work and withholding of test reports or calibration certificates
Who evaluates the significance of the nonconforming work
Who decides about the acceptability of the nonconforming work
Who notifies the customer and recalls work, if necessary
Who is responsible for authorizing the resumption of work
Designate authorities for implementing the corrective action procedure when required

## Slide 7: Process of Root Cause Analysis
Root cause analysis—Using different problem solving methods to identifying the underlying causes of problems or incidents
Who should work on root cause analysis?
  It is best if it is those who are closest to the work on a daily basis
What’s the problem? (DEFINE)
Sometimes “Why” isn’t the starting question
  What is it?
  When did it happened?
  Where did it happen?
  How were overall goals affected?
  Keep it simple—make an outline
  People see problems differently
Why did it happen? (ANALYZE)
What will be done? (PREVENT)

## Slide 8: Examples of Types of Causes/Root Causes
QC out of control—What could be the:
  Cause?-incorrect dilution
  Immediate cause?-pipette on incorrect setting
  Root cause?-pipette not checked before pipetting began
Skinned knee—What could be the:
  Cause?-fell down
  Immediate cause?-bike hit a bump
  Root cause?-didn’t wear protective gear
Water on the floor—What could be the:
  Cause?-leaking freezer
  Immediate cause?-door left open
  Root cause?-freezer not organized
    Items are not easily found
    Takes too long to find items
Root cause means digging deeper for an answer.
Why did this happen?
Cause (first response)
Ask “why” again..
Immediate cause (next response)
Ask “why” again..
Root cause (upon further thought)

## Slide 9: Start with a New Mindset
People are generally not the ultimate cause of problems
People implement processes
Most people do not come to work planning to sabotage their own work
Don’t waste time looking at surface issues
Use passive voice to avoid “blame game”
  Bob didn’t complete the form X correctly (WRONG)
  Form X lacks spaces for all the information
  Form X lacked necessary review and approval (CORRECT)

## Slide 10: One method of Root Cause Analysis: Cause Mapping (5 Whys)
Ask: “Why did this happen?” Write down the response, then ask the question again. Write down the response. Ask the question 5 - 6 times and you may get to the “root cause” of the problem. May ask what and when questions, too:
Why was there water on the floor?
What could be the cause(s)?
Why would that happen?
When could that happen?

## Slide 11: Another method of Root Cause Analysis: Diagramming (Fishbone)
People (manpower)
  Training, verbal miscommunication, lack of communication, staff changed mid-project
Process/Methods
  Procedures, workflow,
  Measurement (Calibrations performed, but were they appropriate?)
Equipment (machines)
  Defective, not maintained, not calibrated, overloaded
Management
  Reviewed annually?
Environment
  Temperature, humidity, work area, distractions
Materials
  Incorrect, degradation, certificates of analysis

## Slide 12: Root Cause Analysis Corrective Action
Once the root cause is identified, you must implement a fix (corrective action) to prevent it from happening again.
  Identify potential corrective actions
  Select and implement the action most likely to eliminate the problem and prevent recurrence
  Corrective actions are appropriate to the magnitude and risk of the problem

## Slide 13: Corrective Action
Once implemented, the laboratory monitors the results of the corrective action to ensure it was effective.
If effective, close the Corrective Action.
If not effective, select another Corrective Action or revisit the root cause.

## Slide 14: Preventive Action
Pro-active process of continual improvement
Goal:
    Improvement of the quality management system
    Improvement of technical operations
    Elimination of potential nonconformities
System improvement stems from rigorously correcting problems, and learning to foresee potential problems.

## Slide 15: Identifying Preventive Actions
May be identified as:
  A result of normal work
  Observations
  Nonconformities
  Analysis of data
  Proficiency tests
  Suggestions for continuous improvement
May be identified for laboratory documents, quality system or laboratory processes

## Slide 16: Addressing Preventive Actions
Develop an action plan
  Specify what situation needs preventive action
  Define what changes/actions need to occur
  Assign responsibility
  Implement the preventive action
Monitor the action
  After implementation gather observations or data to determine whether the preventive action was effective.
If effective, close the Preventive Action.
If not effective, select another Preventive Action

## Slide 17: Summing It Up
Quality management system SOPs define responsibilities and authorities for the root cause investigation process.
Root cause investigation is a problem solving activity focused on the system, not the personnel.
Root cause investigation leads to corrective action, which is intended to prevent recurrence of nonconformance.
Preventive action is a pro-active process intended to prevent occurrence of nonconformance.

## Slide 18: Reference
ISO/IEC 17025:2005 General requirements for the competence of testing and calibration laboratories
https://www.iso.org/standard/39883.html