## Slide 1: A comparison of Nextera XT and Nextera DNA Flex in a Public Health Laboratory 2019 GenomeTrakr Conference
Matt Plumb
Minnesota Department of Health | Infectious Disease Laboratory

## Slide 2: Overview
Comparison of Nextera XT and Nextera DNA Flex
Cost comparison
Our experience and thoughts
Bioinformatic analysis

## Slide 3: MN Department of Health experience with DNA Flex
Piloted DNA flex for Pulsenet late 2018
  Performed 4 runs totaling 96 samples
Revisited DNA flex summer of 2019
  Comparison of XT and Flex

## Slide 4: Cost Comparison
Laboratory Time:
Comparable time spend on Nextera XT and Nextera DNA
DNA Flex may be faster with increased familiarity and skill
Liquid handling robots
Library Preparation Reagent Costs
Item | Uses | Cost | Cost per Use | Cost/sample
Nextera XT DNA Library Preparation Kit (96 samples) | 96 | $3,270.00 | $34.06 | $37.62
NXTR® XT IDX Kt v2 Set A 96 IDXS,384 SMP | 384 | $1,173.00 | $3.05 | 
Ampure Beads (60 mL) | 2400 | $1,200.00 | $0.50 | 
Nextera DNA Flex Library Prep (96 Samples) | 96 | $4,032.00 | $42.00 | $47.00
Nextera™ DNA CD Indexes (96 Indexes, 96 Samples) | 96 | $480.00 | $5.00 | 
Notes: Current list price. Have our contract price at the end.
We already load more than 16 samples per V2 500 cycle kit so samples loaded per cartridge is similar.

## Slide 5: Our experiences and thoughts on DNA Flex
Increased use of beads and magnetic block
Change in tip usage
Increased thermocycler usage
Consistent fragment size after cleanup
Notes: Tech dependent beads
Less 10 tips and more 100 tips
Tagment and tagment stop. 5 min to 15 min. Additional thermocycler usage.
Very consistent ~950bp with pulsenet cleanup protocol
Lot of boxes
Still modify for QC

## Slide 6: Bioinformatic Analysis
Reference mapping and de novo assembly
  Using BWA-MEM and SPADES
BWA v0.7.17-r1188
SPADES v3.12.0
spades.py -k 21,33,55,77,99,127 –careful
Quast v4.3
Samtools v1.9

## Slide 7: Reference mapping
 | Salmonella enterica (6) |  | Escherichia coli (7) | 
 | XT | Flex | XT | Flex
Average Depth | 68.88 | 71.53 | 62.48 | 92.43
Std dev | 19.38 | 16.38 | 37.44 | 46.13
 | Listeria monocytogenes (3) |  | Campylobacter jejuni (4) | 
 | XT | Flex | XT | Flex
Average Depth | 83.83 | 71.15 | 64.25 | 166.29
Std dev | 39.63 | 28.92 | 42.33 | 52.26
 | Vibrio parahaemolyticus (5) |  | Streptococus pyogenes (3) | 
 | XT | Flex | XT | Flex
Average Depth | 84.26 | 85.19 | 88.43 | 136.17
Std dev | 31.57 | 29.66 | 45.43 | 56.14
 | Clostridioides difficile (5) |  |  | 
 | XT | Flex |  | 
Average Depth | 66.83 | 102.88 |  | 
Std dev | 62.09 | 38.95 |  | 

## Slide 8: Reference mapping
 | Salmonella enterica (6) |  | Escherichia coli (7) | 
 | XT | Flex | XT | Flex
% Zero depth | 2.81% | 2.82% | 8.16% | 8.13%
% Depth < 10 | 2.97% | 2.93% | 8.63% | 8.49%
 | Listeria monocytogenes (3) |  | Campylobacter jejuni (4) | 
 | XT | Flex | XT | Flex
% Zero depth | 7.28% | 7.24% | 7.03% | 6.90%
% Depth < 10 | 8.54% | 7.91% | 9.85% | 7.04%
 | Vibrio parahaemolyticus (5) |  | Streptococus pyogenes (3) | 
 | XT | Flex | XT | Flex
% Zero depth | 5.71% | 5.70% | 9.99% | 9.95%
% Depth < 10 | 5.98% | 5.88% | 10.48% | 10.19%
 | Clostridioides difficile (5) |  |  | 
 | XT | Flex |  | 
% Zero depth | 8.65% | 8.51% |  | 
% Depth < 10 | 13.26% | 8.80% |  | 

## Slide 9: De novo assembly
Salmonella enterica
Escherichia coli
 |  | Coverage | Contigs (>500bp) | Largest Contig
Salmonella (6) | XT | 68.88 | 47.17 | 830,264
 | Flex | 71.53 | 38.67 | 853,230
 |  | Coverage | Contigs (>500bp) | Largest Contig
Escherichia coli (7) | XT | 62.48 | 209.57 | 374,564
 | Flex | 92.43 | 208.71 | 365,537
Notes: Very similar

## Slide 10: De novo assembly
Listeria monocytogenes
Campylobacter jejuni
 |  | Coverage | Contigs (>500bp) | Largest Contig
Listeria monocytogenes (3) | XT | 75.89 | 33.33 | 374,564
 | Flex | 79.57 | 10.67 | 365,537
 |  | Coverage | Contigs (>500bp) | Largest Contig
Campylobacter jejuni (4) | XT | 64.25 | 82.00 | 168,368
 | Flex | 166.29 | 33.50 | 339,406
Notes: Flex is noticeably better. Due to coverage in campy?

## Slide 11: De novo assembly
Vibrio parahaemolyticus
Clostridioides difficile
 |  | Coverage | Contigs (>500bp) | Largest Contig
Vibrio parahaemolyticus (5) | XT | 84.26 | 53.20 | 801,202
 | Flex | 85.19 | 39.80 | 794,625
 |  | Coverage | Contigs (>500bp) | Largest Contig
Clostridioides difficile (5) | XT | 71.76 | 212.40 | 169,733
 | Flex | 91.93 | 48.20 | 939,737
Notes: Flex is mildly better for vibrio and extremely better for C. diff

## Slide 12: Would we switch?
Improved bioinformatics
  Greatly improved for Clostridioides difficile
Increased cost
CLIA validated assay using Nextera XT

## Slide 13: Thank you.
Matt Plumb

## Slide 15
Contract Price |  |  |  | 
Item | Uses | Cost | Cost per Use | Cost/sample
NXTR® XT LIB Prep KT PulseNet (96 SMP) | 96 | $2,850.00 | $29.69 | $32.71
NXTR® XT IDX Kt v2 Set A 96 IDXS,384 SMP | 384 | $969.00 | $2.52 | 
Ampure Beads (60 mL) | 2400 | $1,200.00 | $0.50 | 
Nextera DNA Flex Library Prep (96 Samples) | 96 | $3,830.40 | $39.90 | $44.65
Nextera™ DNA CD Indexes (96 Indexes, 96 Samples) | 96 | $456.00 | $4.75 | 

## Slide 16: Reference mapping
Salmonella enterica (6) | XT | Flex |  | Escherichia coli (7) | XT | Flex
Average Depth | 68.882 | 71.535 |  | Average Depth | 62.476 | 92.426
Std dev | 19.381 | 16.375 |  | Std dev | 37.436 | 46.135
# Position with zero depth | 134,929 | 135,494 |  | # Position with zero depth | 378,542 | 377,257
%Position with zero depth | 2.81% | 2.82% |  | %Position with zero depth | 8.16% | 8.13%
# Position with depth =< 10 | 142,884 | 141,035 |  | # Position with depth =< 10 | 400,396 | 394,092
%Position with depth =< 10 | 2.97% | 2.93% |  | %Position with depth =< 10 | 8.63% | 8.49%
Campylobacter jejuni (4) | XT | Flex |  | Listeria monocytogenes (3) | XT | Flex
Average Depth | 64.253 | 166.29 |  | Average Depth | 83.83 | 71.149
Std dev | 42.328 | 52.262 |  | Std dev | 39.634 | 28.92
# Position with zero depth | 115,331 | 113,219 |  | # Position with zero depth | 224,778 | 223,648
%Position with zero depth | 7.03% | 6.90% |  | %Position with zero depth | 7.28% | 7.24%
# Position with depth =< 10 | 161,742 | 115,555 |  | # Position with depth =< 10 | 251,552 | 232,797
%Position with depth =< 10 | 9.85% | 7.04% |  | %Position with depth =< 10 | 8.54% | 7.91%
Notes: Box plots

## Slide 17: Reference mapping
Streptococus pyogenes (3) | XT | Flex |  | Clostridioides difficile (5) | XT | Flex
Average Depth | 88.434 | 136.17 |  | Average Depth | 66.83 | 102.88
Std dev | 45.434 | 56.138 |  | Std dev | 62.09 | 38.95
# Position with zero depth | 185,044 | 184,334 |  | # Position with zero depth | 371,002 | 365,147
%Position with zero depth | 9.99% | 9.95% |  | %Position with zero depth | 8.65% | 8.51%
# Position with depth =< 10 | 194,084 | 188,811 |  | # Position with depth =< 10 | 569,056 | 377,406
%Position with depth =< 10 | 10.48% | 10.19% |  | %Position with depth =< 10 | 13.26% | 8.80%
Vibrio parahaemolyticus (5) | XT | Flex |  | Acinetobacter baumannii (1) | XT | Flex
Average Depth | 84.256 | 85.19 |  | Average Depth | 54.165 | 38.268
Std dev | 31.57 | 29.655 |  | Std dev | 39.069 | 24.298
# Position with zero depth | 187,878 | 187,518 |  | # Position with zero depth | 799,550 | 800,880
%Position with zero depth | 5.71% | 5.70% |  | %Position with zero depth | 18.44% | 18.47%
# Position with depth =< 10 | 196,664 | 193,285 |  | # Position with depth =< 10 | 906,624 | 836,838
%Position with depth =< 10 | 5.98% | 5.88% |  | %Position with depth =< 10 | 20.91% | 19.30%

## Slide 18: De novo assembly
Average |  | Coverage | Contigs (>500bp) | Largest Contig | Total Length | N50 | N75 | L50 | L75
Salmonella (6) | XT | 68.88 | 47.17 | 830,264 | 4,837,399 | 346,807 | 207,441 | 5.17 | 10.17
 | Flex | 71.53 | 38.67 | 853,230 | 4,836,681 | 361,505 | 237,726 | 5.00 | 9.67
Streptococus pyogenes (3) | XT | 88.43 | 15.00 | 556,748 | 1,685,924 | 163,045 | 102,418 | 3.33 | 6.33
 | Flex | 136.17 | 17.00 | 629,943 | 1,686,496 | 163,045 | 87,513 | 3.00 | 6.00
Clostridioides difficile (5) | XT | 71.76 | 212.40 | 169,733 | 4,201,304 | 51,635 | 28,117 | 33.60 | 69.80
 | Flex | 91.93 | 48.20 | 939,737 | 4,209,967 | 387,360 | 260,372 | 4.40 | 8.60
Campylobacter jejuni (4) | XT | 64.25 | 82.00 | 168,368 | 1,672,100 | 77,131 | 40,756 | 10.25 | 20.00
 | Flex | 166.29 | 33.50 | 339,406 | 1,678,832 | 168,410 | 119,491 | 4.25 | 7.50
Listeria monocytogenes (3) | XT | 75.89 | 33.33 | 532,541 | 2,900,189 | 278,706 | 168,273 | 5.33 | 9.67
 | Flex | 79.57 | 10.67 | 1,041,100 | 2,897,166 | 835,948 | 427,034 | 2.33 | 4.00
Vibrio parahaemolyticus (5) | XT | 84.26 | 53.20 | 801,202 | 5,064,205 | 289,824 | 167,241 | 6.40 | 12.80
 | Flex | 85.19 | 39.80 | 794,625 | 5,062,297 | 364,770 | 216,384 | 5.80 | 11.00
Escherichia coli (7) | XT | 62.48 | 209.57 | 374,564 | 5,192,176 | 131,746 | 68,827 | 16.71 | 35.71
 | Flex | 92.43 | 208.71 | 365,537 | 5,211,997 | 132,050 | 69,287 | 16.86 | 36.00
Acinetobacter baumannii (1) | XT | 54.16 | 172.00 | 171,054 | 3,859,635 | 46,435 | 26,355 | 25.00 | 52.00
 | Flex | 38.27 | 141.00 | 171,054 | 3,869,688 | 60,939 | 30,658 | 19.00 | 43.00
Notes: Quast results

## Slide 19: Salmonella enterica
Notes: Very similar

## Slide 20: Escherichia coli
Notes: Very similar

## Slide 21: Listeria monocytogenes
Notes: Differences, flex is better.

## Slide 22: Campylobacter jejuni
Notes: Differences, flex is better.

## Slide 23: Vibrio parahaemolyticus
Notes: Flex is mildly better

## Slide 24: Streptococus pyogenes
Notes: Very similar

## Slide 25: Clostridioides difficile
Notes: Flex is massively better