## Slide 1: QA/QC Through GalaxyTrakr
Errol Strain
FDA Center for Veterinary Medicine
GenomeTrakr Meeting 2019

## Slide 2: Overview
Why Do We Need QC in GalaxyTrakr?
GenomeTrakr/PulseNet Thresholds
  Survey of Pathogen Detection Isolates
Galaxy Workflow
  MicroRunQC
  MicroRunKraken2
Next Steps

## Slide 3: Why QC in Galaxy?
Labs participating in real time pathogen surveillance networks need a check data quality before NCBI submission
  GenomeTrakr, NARMS, Vet-LIRN, PulseNet*
  Detect mistakes/errors as fix them as quickly as possible
Not all labs have a bioinformatician
  Even those with bioinformaticians may want to consider Galaxy
Not all labs have access to bioinformatics software and/or scientific workstations
  GalaxyTrakr runs in AWS, only requirement is Firefox/Chrome browser to connect

## Slide 4: https://galaxytrakr.org
Linux-based computational system that enables users to perform genomic analyses by providing a unified, web-based interface for obtaining genomic data and applying data analysis tools.
HISTORY
TOOLS
INTERFACE

## Slide 5: Quality Thresholds
Quality metric | Salmonella | Listeria | Escherichia/ Shigella | Campylobacter | Vibrio para.
Average read quality Q score for R1 and R2 | >=30 | >=30 | >=30 | >=30 | >=30
Average coverage | >=30X | >=20X | >=40X | >=20X | >=40X
De novo assembly: Seq. length (Mbp) | ~4.4-5.6 | ~2.8-3.1 | 4.2-5.9 | ~1.4-2.2 | ~4.9-5.5
De novo assembly: contigs | <=400 | <=200 | <=600 | <=200 | <=200

## Slide 7
Campy
Listeria
Salmonella
E.coli
Shigella

## Slide 8: SKESA Assemblies (n=201371)
 |  |  | Percentiles |  |  | 
Species | Parameter | Mean | 1% | 5% | 95% | 99%
Campylobacter coli | Length | 1719280 | 1576385 | 1633346 | 1843165 | 1901435
Campylobacter coli | Contigs | 135 | 28 | 39 | 360 | 526
Campylobacter coli | N50 | 67020 | 6689 | 10523 | 162499 | 169540
Campylobacter jejuni | Length | 1680478 | 1574021 | 1596047 | 1776030 | 1818521
Campylobacter jejuni | Contigs | 113 | 32 | 40 | 269 | 455
Campylobacter jejuni | N50 | 64561 | 7918 | 14879 | 140372 | 166390
Escherichia coli | Length | 5055361 | 4252587 | 4379845 | 5426311 | 5536572
Escherichia coli | Contigs | 464 | 107 | 164 | 793 | 1715
Escherichia coli | N50 | 66721 | 5287 | 17503 | 145329 | 191207
Listeria monocytogenes | Length | 2971544 | 2810762 | 2852991 | 3104566 | 3163466
Listeria monocytogenes | Contigs | 92 | 16 | 20 | 303 | 784
Listeria monocytogenes | N50 | 259825 | 7517 | 23731 | 541796 | 1458094
Salmonella enterica | Length | 4753724 | 4466741 | 4546637 | 4998221 | 5145413
Salmonella enterica | Contigs | 208 | 37 | 49 | 485 | 1857
Salmonella enterica | N50 | 108720 | 4246 | 21773 | 266999 | 403435
Shigella flexneri | Length | 4400771 | 4234124 | 4318545 | 4479041 | 4516205
Shigella flexneri | Contigs | 571 | 384 | 420 | 748 | 1267
Shigella flexneri | N50 | 24238 | 7478 | 15244 | 29074 | 33535

## Slide 9: SKESA Assemblies (Salmonella n=139901)
 |  |  | Percentiles |  |  | 
Species | Parameter | Mean | 1% | 5% | 95% | 99%
Salmonella enterica | Length | 4753724 | 4466741 | 4546637 | 4998221 | 5145413
Salmonella enterica | Contigs | 208 | 37 | 49 | 485 | 1857
Salmonella enterica | N50 | 108720 | 4246 | 21773 | 266999 | 403435
Quality metric | Salmonella
De novo assembly: Seq. length (Mbp) | ~4.4-5.6
De novo assembly: contigs | <=400
8% of data would fail based on # of contigs
35 out of 139901 > 5.6MB

## Slide 10: SKESA Assemblies (Ecoli = 39315, Shigella=1018)
 |  |  | Percentiles |  |  | 
Species | Parameter | Mean | 1% | 5% | 95% | 99%
Escherichia coli | Length | 5055361 | 4252587 | 4379845 | 5426311 | 5536572
Escherichia coli | Contigs | 464 | 107 | 164 | 793 | 1715
Escherichia coli | N50 | 66721 | 5287 | 17503 | 145329 | 191207
Shigella flexneri | Length | 4400771 | 4234124 | 4318545 | 4479041 | 4516205
Shigella flexneri | Contigs | 571 | 384 | 420 | 748 | 1267
Shigella flexneri | N50 | 24238 | 7478 | 15244 | 29074 | 33535
Quality metric | Escherichia/ Shigella
De novo assembly: Seq. length (Mbp) | 4.2-5.9
De novo assembly: contigs | <=600
E.coli – 1 out of 39315 > 5.9
E.coli – 18% failure
Shigella – 22% failure

## Slide 11: SKESA Assemblies (Cc =677 , Cj=3213)
 |  |  | Percentiles |  |  | 
Species | Parameter | Mean | 1% | 5% | 95% | 99%
Campylobacter coli | Length | 1719280 | 1576385 | 1633346 | 1843165 | 1901435
Campylobacter coli | Contigs | 135 | 28 | 39 | 360 | 526
Campylobacter coli | N50 | 67020 | 6689 | 10523 | 162499 | 169540
Campylobacter jejuni | Length | 1680478 | 1574021 | 1596047 | 1776030 | 1818521
Campylobacter jejuni | Contigs | 113 | 32 | 40 | 269 | 455
Campylobacter jejuni | N50 | 64561 | 7918 | 14879 | 140372 | 166390
Quality metric | Campylobacter
De novo assembly: Seq. length (Mbp) | ~1.4-2.2
De novo assembly: contigs | <=200
C.coli – 16% failure
C.jejuni – 10% failure

## Slide 12: SKESA Assemblies (Listeria - 17247)
 |  |  | Percentiles |  |  | 
Species | Parameter | Mean | 1% | 5% | 95% | 99%
Listeria monocytogenes | Length | 2971544 | 2810762 | 2852991 | 3104566 | 3163466
Listeria monocytogenes | Contigs | 92 | 16 | 20 | 303 | 784
Listeria monocytogenes | N50 | 259825 | 7517 | 23731 | 541796 | 1458094
Quality metric | Listeria
De novo assembly: Seq. length (Mbp) | ~2.8-3.1
De novo assembly: contigs | <=200
9% Failure
5.9% > 3.1 MB

## Slide 13: QC in GalaxyTrakr
Create list of pairs for MiSeq runs
Note – Must specify filters in filenames that indicate forward and reverse reads
Goal – Assess sequence quality and confirm identity (species/sequence type)

## Slide 14: MicroRunQC
Shared Data -> Workflows

## Slide 15: What to Check? SKESA
# of contigs, total length of contigs, estimated coverage, N50, median insert size
Mixture
Poor assembly, low coverage

## Slide 16: What to check? MLST
Species
Different sources typically have different sequence types

## Slide 17: What to check? MLST
Low quality run (575 contigs, 21X coverage) – Questionable allele calls
Mixture

## Slide 18: MicroRunKraken2

## Slide 19: MicroRunKraken2

## Slide 20: MicroRunKraken2
Sample | Name | TaxaID | Rank | FragRank | FragTotal | PercentageTotal
SRR1363307 | Salmonella | 590 | G | 6548 | 572873 | 91.36
SRR1363307 | Salmonella enterica | 28901 | S | 455179 | 566307 | 90.31
SRR2074986 | Salmonella | 590 | G | 8564 | 391850 | 88.78
SRR2074986 | Salmonella enterica | 28901 | S | 332544 | 383210 | 86.82
SRR3049944 | Salmonella | 590 | G | 15933 | 829921 | 95.56
SRR3049944 | Salmonella enterica | 28901 | S | 762378 | 813937 | 93.72
SRR3644931 | Listeria | 1637 | G | 38926 | 1240373 | 98.55
SRR3644931 | Listeria monocytogenes | 1639 | S | 1192069 | 1200811 | 95.4
SRR4116047 | Escherichia | 561 | G | 25558 | 1210591 | 71.34
SRR4116047 | Escherichia coli | 562 | S | 1124483 | 1183573 | 69.75
SRR5409483 | Listeria | 1637 | G | 25543 | 389012 | 89.24
SRR5409483 | Listeria monocytogenes | 1639 | S | 360159 | 363164 | 83.31
SRR5409483 | Enterococcus | 1350 | G | 7059 | 34351 | 7.88
SRR5725229 | Salmonella | 590 | G | 4753 | 1041155 | 91.28
SRR5725229 | Salmonella enterica | 28901 | S | 801763 | 1036286 | 90.86
SRR7788264 | Escherichia | 561 | G | 31872 | 628317 | 52.74
SRR7788264 | Escherichia coli | 562 | S | 590514 | 594245 | 49.88
SRR8914694 | Campylobacter | 194 | G | 55678 | 480702 | 99.22
SRR8914694 | Campylobacter jejuni | 197 | S | 383644 | 421806 | 87.07
SRR10068115 | Campylobacter | 194 | G | 106513 | 684754 | 40.02
SRR10068115 | Campylobacter jejuni | 197 | S | 262821 | 270341 | 15.8
SRR10068115 | Campylobacter helveticus | 28898 | S | 242300 | 242300 | 14.16

## Slide 23: MicroRunKraken2
Species | Mean % | 1% | 5% | 95% | 99%
S. enterica | 85 | 65 | 72 | 94 | 95
E. coli | 42 | 11 | 20 | 59 | 69
C. jejuni | 71 | 60 | 64 | 82 | 87
S. flexneri | 12 | 8 | 9 | 21 | 23
C. coli | 72 | 54 | 62 | 82 | 86
L. monocytogenes | 86 | 70 | 75 | 94 | 95

## Slide 24: What’s Next?
We need to increase reliability of GalaxyTrakr service
  Slow downs during peak usage
Provide cgMLST matching tool
  What is the nearest neighbor from Pathogen Detection/SRA
Provide phenotypic/functional information
  AMRfinder

## Slide 25: Thank You
CFSAN
Justin Payne
Charles Strittmatter
Hugh Rand
Jimmy Sanders
James Pettengill
Arthur Pightling
Yan Luo
Yu Wang
Joseph Baugher
Jayanthi Gangiredla
Tom Farrell
Kelly Bunning
CVM
Pat McDermott
Chih-Hao Hsu
Claudia Lam
Gordon Martin
Jason Abbott