## Slide 1: Sample Handling and Assuring the Quality of Test Results
ISO/IEC 17025, clauses 5.8 and 5.9

## Slide 2: Abbreviations and Acronyms
QC-Quality control

## Slide 3: What will be covered in this training?
Sample Handling
  What does this encompass?
  What does the laboratory need to consider?
Quality Control (QC)
  Requirements of ISO/IEC 17025
  What happens when QC fails?
  Proficiency testing

## Slide 4: Connections
How are sample handling and QC related to each other?
  Results are only as good as the sample which is tested
  Ensuring proper sample handling supports the validity of testing
  Sample handling and QC also play a part in regulatory work by ensuring sample integrity and data defensibility

## Slide 5: Sample Handling
  5.8.1 The laboratory shall have procedures for the transportation, receipt, handling, protection, storage, retention, and/or disposal of test items, including all provisions necessary to protect the integrity of the test item, and to protect the interests of the laboratory and the customer.
    This also means the laboratory must be aware of any customer requirements for sample handling
ISO/IEC 17025 clause 5.8

## Slide 6: Sample Handling
  5.8.2 The laboratory shall have a system for identifying test items:
    Retain the identification on the sample throughout its time in the laboratory (including conditions such as freezing, autoclaving, etc.)
    Procedures to avoid mixing up samples physically or in records
    Address subdividing samples and retaining identity
    Address how to transfer items within and from the laboratory

## Slide 7: Sample Handling
  5.8.3 Upon receipt of a sample the laboratory must:
    Record abnormalities or departures from normal or specified sample conditions
    Consult the customer if samples may not be suitable for testing, do not conform to the description provided, or the requested test is not specified in sufficient detail
    Discussions with the customer and instructions received from the customer must be recorded

## Slide 8: Sample Handling
  5.8.4 The laboratory must have procedures and facilities for avoiding deterioration, loss, or damage to the test item during storage, handling, and preparation.
    Any handling instructions that come with the sample must be followed
    If samples must be stored or conditioned under specific environmental conditions, these conditions must be maintained, monitored, and recorded
    The laboratory must be able to store and secure samples if required to maintain their integrity

## Slide 9: Ensuring the quality of test results
5.9 The laboratory must have QC procedures
  To monitor validity of testing (plan the monitoring, review the results) to ensure:
    Accuracy
    Precision
  Record QC results so that trends can be detected
  Apply statistical techniques to review of QC data, where practical

## Slide 10: What does ISO/IEC 17025 require as a QC sample?
The standard does not require any particular QC sample. These are dictated by test methods and accreditation bodies.
The standard recommends use of the following :
  Certified Reference Materials
  Internal QC using secondary Reference Materials
  Participation in proficiency testing or interlaboratory comparison programs
  Replicate tests
  Retesting retained samples
  Correlation of results for different characteristics of a item

## Slide 11: Most Accrediting Bodies Require Procedures and Documentation for:
Reagents, Reference Materials and Reference Standards
Manufacturer
Purity
Date of Receipt
Storage conditions
Expiration
Prepared by
Dates of Use
Certificate of Authenticity
Transport
How to Purchase
Unique Identifier

## Slide 12: What happens when QC fails?
When QC is outside predefined criteria, planned action must be taken to:
  Correct the problem
  Prevent incorrect results from being reported
Key terms:
  Predefined criteria: The laboratory must define acceptance criteria for its routine QC
  Planned action: The laboratory must specify what to do if QC fails to meet acceptance criteria. This may be corrective action

## Slide 13: Proficiency Testing
ISO/IEC 17025 does not require any particular amount or frequency of proficiency testing
Accrediting bodies have their own requirements for amount and frequency of proficiency testing that laboratories must follow

## Slide 14: Summing it up: Sample Handling
Who receives it?
Are there special precautions in handling/storage?
Write procedures for recording relevant data/information
Ensure staff are trained and authorized in all procedures
How is the sample transported?
Temperature
Humidity
Disposal
Unique ID
Entry into LIMS
Courier
Mail
Who authorizes?
What method is used?
Sample handling includes ensuring the laboratory meets customer requirements, protects sample integrity, and provides appropriate security of samples

## Slide 15: Summing it up: QC
QC— A system that compares performance against specific requirements and defined standards
QC data must be monitored, reviewed, and analyzed
Failing QC requires action
Proficiency testing is part of the laboratory’s overall QC plan

## Slide 16: Reference
ISO/IEC 17025:2005
  https://www.iso.org/standard/39883.html