## Slide 1: Whole Genome Sequencing: the Compliance Perspective
Leslie Hintz
Pathogen Subject Matter Expert (SME)
Office of Compliance and Enforcement
Human Foods Program (HFP)
U.S Food and Drug Administration (FDA)

## Slide 2: Pathogen Findings
Determine close relationships with pathogens in FDA regulated foods and manufacturing environments:
    Environmental Samples
    Finished Product Samples
    Clinical isolates
FDA Recall data shows the top 2 reasons for a product recall
  Allergens- Misbranding
  Pathogens in RTE Foods (Salmonella, Listeria monocytogenes)

## Slide 3
Facilities not controlling the pathogen risk in processing environment.
    Ineffective sanitation programs
        Cross contamination
        Condensate/ high pressure hoses/ roof leaks/ etc.
        Bad equipment design to effectively clean/ sanitize
        Product flow (“pretzel flow” vs hygienic design)
            State of the art cleaning procedures won’t fix underlying problem
Preventable with environmental monitoring programs and verification procedures
FDA Findings
Environmental Microbial Risk

## Slide 4: Regulatory Considerations
All regulatory actions are considered on a case-by-case assessment of the evidence and findings
A finding of a pathogen in an environmental sample collected from:
  A food contact surface located post ‘kill step’ or where bacterial contamination is not subsequently controlled.
  Non-food contact surfaces coupled with other indications of insanitary conditions and/or failure to adhere to good manufacturing practices.
  A genetic match that connects a bacterial strain found in an environmental sample and a bacterial strain from an ill person.
  A genetic match that connects environmental isolates obtained on two separate occasions from the same establishment, indicating that a facility may have a potential harborage of a pathogen in a food processing environment and/or that a facility is not adequately controlling environmental pathogens.
  A genetic match that connects an environmental isolate and a food isolate from the same establishment. Once again, this is a scenario where a recall of the affected food may be warranted to protect consumers, and food likely to be affected in a similar manner must also be assessed.

## Slide 5: Preventive Controls for Human Food
  Hazard Analysis and Food Safety Plan- knowing the risks and hazards needing to be controlled and how to ensure they are controlled throughout the process.
  Sanitation controls- knowing the procedures, practices, and processes to significantly minimize or prevent the hazards such as environmental pathogens, biological hazards due to employee handling, and food allergen hazards.
    Verification of adequate sanitation controls through environmental monitoring
  Supplier controls- knowing contract manufacturers, ingredient suppliers, and how they control the risk.

## Slide 6: Case Study

## Slide 7
FDA will be outward reaching/ sharing what we know
  Conversation about the signal (result)
  Provides a signal for industry as well
What environmental monitoring program do you have?
What corrective actions (ex. a root cause analysis, etc.) are done in the event a positive may be found?
What Happens Next?

## Slide 8
If cleaning/ sanitation inadequate-
    may suggest a different conversation from FDA
Prevention through supplier controls-
    know your contract manufacturers, ingredient suppliers- how they control the risk
If you have zero/ minimal data of your own-
    may suggest a different conversation from FDA
    FDA may conduct swabbing-
        different then the places we are already out swabbing
Next Steps

## Slide 9
  We expect you to find it
    It’s about what happens next!
        Look in Zone 1/ food contact surfaces
        Find and fix
        Reacting to Zone 2, 3, and 4s before it gets into Zone 1
  It is doable!
    # of success stories where firms have strong EMP and operating in control
    It’s all about the data
Lessons Learned

## Slide 10: U.S. Food and Drug Administration, Human Foods Program logo