## Slide 1
QMS Quick Learning Activity
www.aphl.org
Equipment and Calibration
ISO/IEC 17025:2017

## Slide 2: Terms & Acronyms
Calibration-the comparison of two measurement devices or systems (one of known uncertainty [your standard] and one of unknown uncertainty [your test equipment])
Equipment- Those items of equipment necessary to perform a test and which have a significant effect on the uncertainty of measurement of test results
SOP-Standard Operating Procedure
Traceability-the property of a measurement result whereby the result can be related to a reference through a documented unbroken chain of calibrations, each contributing to the measurement uncertainty
Traceability to the SI (International System of Units)- metrological traceability to a measurement unit of the International System of Units
– Test equipment calibration is traceable to the SI through US National Institute Standard of Technology (NIST) (not traceable to NIST)

## Slide 3: Some distinctions
Policies “What we do”
Processes “How it happens”
Procedures and Job Aids
“How to do it”
Forms & Records “What happened”

## Slide 4: Equipment
6.1 The laboratory shall have the following available which are necessary to manage and perform its laboratory activities.
Personnel
Facilities
Equipment
Systems
Support services

## Slide 5: Equipment: LIMS and Software (Control your Data!)
Calculations (manual and electronic) and data transfers shall be checked in an appropriate and systematic manner.
Laboratory information management system(s) (LIMS) used for the collection, processing, recording, reporting, storage, or retrieval of data, the laboratory shall ensure that:
  They are maintained in a manner that ensure the integrity of the data and information:
    Excel spreadsheets with calculations only (documents)— Lock the formula cells
    Excel spreadsheets with results after calculations (records)—pdf the record so no changes can be made

## Slide 6: Protect Your Data!
Establish and implement procedures to protect your LIMS and data from:
  Unauthorized use
  Unauthorized changes
  Against tampering and loss
Commercial software (e.g., word processing, database, statistical programming) is considered sufficiently validated
Laboratory software and modifications to commercial off-the-shelf software must be authorized, documented, and validated before use

## Slide 7: LIMS
The LIMS shall be operated in an environment that complies with provider and laboratory specification, and which safeguard the accuracy of recording and (if manual) transcription
The LIMS shall include recording system failures and appropriate immediate and corrective actions
The laboratory shall ensure that external LIMS management providers shall comply with applicable ISO/IEC 17025 requirements
All instructions, manuals, and reference data for the LIMS shall be available to personnel.

## Slide 8: Equipment
The laboratory shall have access to equipment that is required for the correct performance of laboratory activities and that can influence the results
The laboratory shall establish a calibration program, which shall be reviewed and adjusted as necessary in order to maintain confidence in the status of calibration.
Equipment & Software:
  Capable of achieving accuracy and/or measurement uncertainty to provide valid result
  Verified prior to placing into service
    Meets specification requirements
    Records must be kept
  Calibrated when
    Measurement accuracy or uncertainty affects the validity of the reported results
    To establish metrological traceability of the reported results

## Slide 9: Who should operate equipment?
Equipment shall be operated by authorized personnel using up- to-date manuals containing:
  Instructions for use and maintenance
  Procedures for safe handling, transport, storage, use and planned maintenance to ensure proper functioning and to prevent contamination or deterioration
Please see your Equipment SOPs for further guidance

## Slide 10: Equipment Needs & Documentation
All measurement and testing equipment have a significant effect on the validity and accuracy of test results
All equipment that requires calibration shall be labelled, coded, or otherwise identified to indicate the status of calibration, including the last date of calibration and date of expiration or due date of next calibration
Equipment sent out of the laboratory must be recalibrated or checked and shown to be satisfactory before placing into service

## Slide 11: Equipment Needs & Documentation
When calibration and reference material data include reference values or correction factors, the laboratory shall ensure these are updated and implemented
The laboratory takes practicable measures to prevent unintended adjustments of hardware and software from invalidating results.
Calibration and verification takes place at specified intervals through the use of traceable standards or appropriate reference materials or reference cultures

## Slide 12: Keep Records
Records shall be maintained for each item of equipment & software significant to the tests and contain
Identity including version
Manufacturers' name
Or other unique ID
Serial number
Checks that the equipment complies with specifications
Manufacturer’s instructions (manuals)
Current location
Records
Dates, results, and copies of calibrations, maintenance, & reference materials
Reports and results
Plans
Adjustments
Acceptance criteria
Relevant dates & period of validity
Any damage, malfunction, modification or repair
QMS Quick Learning Activity

## Slide 13: Defective Equipment
Equipment that has been overloaded or mishandled, gives suspect results, is defective, or outside specified requirements shall be taken out of service, isolated or clearly marked as being out of service until it has been repaired & recalibrated, & verified.
The laboratory shall examine the effect or deviation on test results and initiate management of nonconforming work procedure.
DEFECTIVE EQUIPMENT
TAKEN OUT OF SERVICE

## Slide 14: Metrological Traceability & Equipment
ning Activity
The laboratory shall establish and maintain metrological traceability of its measurement results by means of a documented unbroken chain of calibrations, each contributing to the measurement uncertainty, linking them to an appropriate reference.
  traceable standards
  or appropriate reference materials
  or reference cultures
Traceability applies to measuring and test equipment unless you can prove that it is a minor component of measuring uncertainty. In
QMS Quick Lear
13

## Slide 15: What is Calibration?
QMS Quick Learning Activity
A response to a known value which establishes a relationship between the known value and an indicator and established tolerance
"I have the result, I know what it should be—what is my answer in relation to the known value and how much can I tolerate the difference?"
Tolerance (+ or -)
End result

## Slide 16: Intermediate Checks
QMS Quick Learning Activity
There need to be defined procedures and schedules for carrying out checks needed to maintain confidence in the calibration status of:
  Reference standards
  Primary standards
  Working standards
  Transfer standards
  Reference materials

## Slide 17: Things to Document for Analysis
QMS Quick Learning Activity
Instrument
Unique ID
Conditions
Temperature
Column, other consumables
Quality Control (QC)
Method blank
Spikes
Continuing calibration
QC: Laboratory control samples (LCS);
how prepped, lot numbers, expiration, etc.

## Slide 18: Support Equipment that require calibration
QMS Quick Learning Activity
Support equipment requiring calibration includes:
  Balances
  Ovens
  Refrigerators
  Freezers
  Incubators
  Water baths
  Temperature measuring devices
  Thermal/pressure sample preparation devices
  Volumetric dispensing devices (including automatic dilutor/dispensing devices)
  Centrifuges
If quantitative results are dependent on their accuracy

## Slide 19
Support Equipment
Date of Use Verification
Maintained in proper working order. Keep records of repair and maintenance
Calibrated or verified annually using a recognized SI traceable reference
Remove from service until repaired or use established correction factors
Raw data records shall be retained to document equipment performance
On each day of use, equipment shall be checked and documented
Volumetric devices (except Class A glassware and Glass microliter syringes) shall be checked on a planned basis

## Slide 20: Some questions to ask for equipment
Is there a system with a procedure on commissioning equipment, verifying its performance, and calibration prior to use?
What is the plan/procedure for continuing calibration and verification of the equipment’s performance?
Are there records that show the continuing calibration and verification is ongoing on regularly scheduled intervals?
Are there labels that a user may see immediately to determine the status of the regular checks and calibrations?

## Slide 21: References
ISO/IEC 17025:2017
  https://www.iso.org/standard/66912.html