## Slide 1: Internal Auditing and Control of Nonconforming Work
ISO/IEC 17025:2017
Clauses 8.8 and 7.10

## Slide 2: What will be covered in this training?
Internal Auditing
  What is it?
  Who performs it?
  What are the possible outcomes?
Control of Nonconforming Work
  What is it?
  How do I identify it?
  What do I do if it happens?

## Slide 3: Terms, Acronyms, and Definitions
Audit (assessment): The on-site verification activity, such as inspection or examination, of a process or quality system, to ensure compliance to requirements. An audit can apply to an entire organization or might be specific to a function, process or production step
Correction: The immediate fix to the problem
Corrective Action (CA): Need to dig deeper to find out “WHY”
Documents: “Say” what you are going to do
Nonconforming work: When any aspect of its laboratory activities or results of this work do not conform to its own procedures or the agreed requirements of the customer

## Slide 4: Terms, Acronyms, and Definitions
Opportunities for Improvement: Actions taken to enhance quality of a process; can be used to prevent potential future occurrences of a nonconformance
Quality Management System Audit: A systematic, independent examination and review to determine whether quality activities and related results comply with plans and whether these plans are implemented effectively and are suitable to achieve the objectives
Quality Management System (QMS): The quality, administrative, and technical systems that govern the operations of the laboratory
Records: “Proof” of what you are doing
Root Cause: A factor that caused a nonconformance and should be permanently eliminated through process improvement

## Slide 5: Connections
How are internal audits and nonconforming work related to each other?
  Internal audits look for compliance with the ISO/IEC 17025 standard and quality management system. Compliance is also called conformance.
  Nonconformances can be identified by internal audits, and also found in other ways.

## Slide 6: Internal Audit
  8.8.1 The laboratory shall conduct internal audits at planned intervals to provide information on:
    whether the management system conforms to:
      the laboratory’s own requirements for its management system, including the laboratory activities;
      the requirements of ISO/IEC 17025; and
    whether the management system is effectively implemented and maintained.
ISO/IEC 17025 clause 8.8

## Slide 7: ISO/IEC 17025:2017 Auditing Requirements
Audits shall be planned, established, implemented, and maintained in an audit program which shall take into account:
  Frequency
  Methods
  Responsibilities
  Planning requirements
  Reporting
Audit shall take into consideration the importance of the laboratory activities concerned.

## Slide 8: ISO/IEC 17025:2017 Auditing Requirements
Audits shall also take into consideration changes affecting the laboratory.
Results of previous audits shall also be reviewed and considered.
The laboratory shall:
  Define the audit criteria and scope for each audit
  Ensure that the results are reported to management
  Implement appropriate correction and corrective actions without delay
  Retain records as evidence of the implementation of the audit program and the results

## Slide 9: ISO/IEC 17025:2017 Auditing Requirements
Audits should be carried out by trained and qualified personnel who are, wherever resources permit, independent of the activity to be audited.
  Note: The cycle for internal auditing should normally be completed in one year. Check with your accrediting body for specific requirements.

## Slide 10: ISO/IEC 17025:2017 Auditing Requirements
  8.7.1(d) Follow-up audit activities shall verify and record the implementation and effectiveness of the corrective action taken.
  8.9.2 Outcome of recent internal audits shall be included in the management review

## Slide 11: ISO/IEC 17025:2017 Auditing Requirements-Periodic reviews
  6.3.4 Implementation and monitoring of measures to control facilities including
    Access to and use of areas affecting laboratory activities
    Prevention of contamination, interference, or adverse influences on laboratory activities
    Effective separation between areas with incompatible laboratory activities
  6.3.5 Activities at sites or facilities outside its permanent control

## Slide 12: ISO/IEC 17025:2017 Auditing Requirements-Periodic reviews
6.4.7 The calibration program shall be reviewed and adjusted as necessary
6.6.2 The laboratory’s requirements for externally provided products and services shall be reviewed and records retained.
7.2.1.6 Periodic review of method development to confirm that the needs of the customer are still being fulfilled.

## Slide 13: ISO/IEC 17025:2017 Auditing Requirements-Periodic reviews
7.7.2 The laboratory shall monitor its performance by comparison of results of other laboratories (i.e., participation in proficiency testing or interlaboratory comparisons), and this monitoring shall be planned and reviewed.

## Slide 14: ISO/IEC 17025:2017 Auditing Requirements-Periodic reviews
8.6.1 The laboratory shall identify and select opportunities for improvement and implement any necessary actions.
NOTE: Opportunities for improvement can be identified through the review of the operational procedures, the use of the policies, overall objectives, audit results, corrective actions, management review, suggestions from personnel, risk assessment, analysis of data, and proficiency testing results.

## Slide 15: Internal Auditors look for:
Does the laboratory “say” what they do?
  Do we have written documents (policies, procedures, arrangements) that meet the requirements of ISO/IEC 17025?
Does the laboratory “do” what we say?
  Are we in compliance with our own management system, the ISO/IEC 17025 standard, and our technical SOPs?
Can the laboratory “prove” it with records?
  Training records, standard preparation records, work books, customer reports, and audit reports are all examples of records (proof) that the laboratory is “doing what we say”.

## Slide 16: Purpose of Internal Audits:
Provide assurance to management that the quality management system is implemented as intended.
Identify opportunities for improving the management system itself and its effectiveness.
Find problems before they affect quality of data.
Prepare for external audits.
Can be used as training tool.
Internal auditing is a requirement of ISO/IEC 17025 Standard

## Slide 17: Basic Internal Audit Process
The audit schedule
The audit checklist
The auditors
Do
The audit as scheduled
Ask the questions
Examine the records
Check
Degree of conformity
Act
Cite non-compliances if found
Implement Corrective Action
Plan
Usually planned by QA Manager
Conducted by trained auditor, independent of area being audited
Does the laboratory meet requirements of ISO/IEC 17025 and its own SOPs?
Findings include compliance, noncompliance, and opportunities for improvement

## Slide 18: Audit the System, NOT the People
Gather objective evidence
  Policies, SOPs, records, auditor observation
Interview the people
  Understand the system and its effectiveness
  How do they:
    Receive and interpret information
    Carry out instructions
    Produce the data
If nonconformances arise, fix that system
  Very few problems are due to the people
  The better the system, the fewer times people will be the problem

## Slide 19: Control of Nonconforming Work
  7.10.1 The laboratory shall have a procedure that shall be implemented when any aspect of its laboratory activities or results of this work do not conform to its own procedures or the agreed requirements of the customer
ISO/IEC 17025:2017 clause 7.10

## Slide 20: Control of Nonconforming Work
  The procedure:
    Defines responsibilities & authorities for managing nonconforming work
    Ensures actions taken for managing when nonconforming work (i.e., halting work, withholding reports) are based on established risk levels
    Ensures evaluation of the significance of nonconforming work is made; including an impact analysis on previous work
    Ensures that a decision is made if the nonconforming work is acceptable
    Ensures the customer is notified and work is recalled. if needed
    Defines responsibility for authorizing resumption of work
ISO/IEC 17025:2017 clause 7.10.1

## Slide 21: Control of Nonconforming Work
  7.10.3 Where the evaluation indicates that the nonconforming work could recur, or that there is doubt about the conformity of the laboratory’s operations with its own management system, the laboratory shall implement corrective action.
    7.10.1 (previous slide) required correction to always be taken when nonconforming work identified
    7.10.3 (this slide) only requires corrective action in certain circumstances
ISO/IEC 17025:2017 clause 7.10.3

## Slide 22: Control of Nonconforming Work
  The laboratory shall retain records of nonconforming work and actions as specified in 7.10.1
ISO/IEC 17025:2017 clause 7.10.2
Records

## Slide 23: What is nonconforming work?
Requires evidence that a specific requirement was not met
Non-fulfillment of a requirement
When any aspect of testing or other work does not comply to procedures (the laboratory’s own procedures or those of the customer’s)
Out-of-control Quality Control
Incorrect results reported
Failing proficiency test

## Slide 24: What is nonconforming work?
  In 6.4.9 :
  Equipment that has been subjected to overloading or mishandling, gives questionable results, or has been shown to be defective or outside specified requirements, shall be taken out of service.
  The laboratory shall examine the effect of the defect or deviation from specified requirements and shall initiate the management of nonconforming work procedure.

## Slide 25: How is a nonconformance is identified?
Audit
Customer complaint/feedback
Quality Control data
Proficiency test results
Observation/self-reporting

## Slide 26: How to respond to nonconforming work
Quality management system SOP (procedure) defines who can identify it and who is notified
Based on risk level:
  Should work be halted?
  Must data be withheld/reports recalled?
Evaluate the significance of the nonconformity
Correct it
Notify the customer and recall work, if needed
Resume work as determined by authorized person

## Slide 27: Correction vs. Corrective Action
Correction
  An action to eliminate one instance of a nonconformity
  Does not identify causes
  Immediate fix
Corrective Action
  An action to identify and eliminate the cause of a nonconformity so that it will not happen again
  Prevent recurrence
  Problem solving process

## Slide 28: Correction Examples
Quality control (QC) samples fail:
  Correction: Reanalyze the QC sample and all samples since the last QC was in control
Failure to complete all scheduled audits during the time period specified in quality management system
  Correction: Conduct the audits that were missed

## Slide 29: After the correction
Resume work and release data when appropriate and with proper authorization.
If deemed necessary, begin root cause analysis and corrective action process.
  Note: this is covered in a separate QMS Quick Learning Module

## Slide 30: Summing it up
Internal audits are planned activities, with the goal of assuring compliance to ISO/IEC 17025 and the laboratory’s policies and procedures.
A nonconformance requires immediate correction, along with additional decisions about significance of the nonconformity and acceptability of the work.

## Slide 31: Reference
ISO/IEC 17025:2017 General requirements for the competence of testing and calibration laboratories
–https://www.iso.org/standard/39883.html