## Slide 1: Nonconforming Work, Root Cause Analysis, Corrective Actions, and Opportunities for Improvement ISO/IEC 17025:2017 Clauses 7.10, 8.6, and 8.7

## Slide 2: What will be covered in this training?
Root Cause Analysis
  What it is
  Who performs it
  Sample methods for root cause analysis
Corrective Action
  What is it?
Opportunities for Improvement
  Customer Feedback

## Slide 3: Definitions
Continual Improvement: recurring activity to increase the ability to fulfill requirements
Correction: immediate action to eliminate a detected nonconformity
Corrective Action: action to eliminate the cause of a detected nonconformity or other undesirable situation
Effectiveness: extent to which planned activities are realized and planned results achieved
Nonconformance: nonfulfillment of a requirement
Nonconforming work: when work does not conform to the laboratory’s procedures or agreed requirements with the customer)

## Slide 4: Root Cause Analysis
Root Cause Analysis/Investigation
  A type of problem solving method aimed at identifying the root cause(s) of a problem (nonconformance)
  The goal is to prevent recurrence of the nonconformance
  Is not a quick and easy process that can always be accomplished in an office or conference room
  Generally requires talking to the people involved who best know the process

## Slide 5: Root Cause Analysis
Section 7.10.3
Takes place after the immediate correction of a nonconformance.
Required when a nonconformance is significant (it could recur; it casts doubt on a laboratory operation’s compliance with its own quality management system)
Required for nonconformances identified through audits and for failing proficiency test reports.

## Slide 6: Laboratory SOP Must Define Authorities and Responsibilities
Section 7.10.1
Responsibility and authority for the management of nonconformances
Actions to be taken when nonconforming work is identified
  This may include halting or repeating of work and withholding of test reports
Who evaluates the significance of the nonconforming work
Who decides about the acceptability of the nonconforming work
Who notifies the customer and recalls work, if necessary
Who is responsible for authorizing the resumption of work
Designate authorities for implementing the corrective action procedure when required

## Slide 7: Laboratory SOP Must Define Authorities and Responsibilities
Where the evaluation indicates that the nonconforming work could recur, or that there is doubt about the conformity of the laboratory's operations with its own management system, the laboratory shall implement corrective action.
First step: React to the nonconformity
  Take action to control and correct it
  Address the consequences
Next step: Root Cause Analysis for the cause

## Slide 8: Nonconforming Work and Next Steps
Sections 7.10 and 8.7.1
Where the evaluation indicates that the nonconforming work could recur, or that there is doubt about the conformity of the laboratory's operations with its own management system, the laboratory shall implement corrective action.
First step: React to the nonconformity
  Take action to control and correct it
  Address the consequences
Next step: Root Cause Analysis for the cause of the nonconformity.

## Slide 9: Next Steps
Evaluate the need for action to eliminate the cause(s) of the nonconformity so that it does not recur
  Review and analyze the nonconformity
  Determine the cause
  Determine if similar nonconformities exist or could potentially occur

## Slide 10: Process of Root Cause Analysis
Root cause analysis—Using different problem-solving methods to identifying the underlying causes of problems or incidents
Who should work on root cause analysis?
  It is best if it is those who are closest to the work on a daily basis
What’s the problem? (DEFINE)
Sometimes “Why” isn’t the starting question
  What is it?
  When did it happened?
  Where did it happen?
  How were overall goals affected?
  Keep it simple—make an outline
  People see problems differently
Why did it happen? (ANALYZE)
What will be done? (PREVENT)

## Slide 11: Examples of Types of Causes/Root Causes
QC out of control—What could be the:
  Cause?-incorrect dilution
  Immediate cause?-pipette on incorrect setting
  Root cause?-pipette not checked before pipetting began
Skinned knee—What could be the:
  Cause?-fell down
  Immediate cause?-bike hit a bump
  Root cause?-didn’t wear protective gear
Water on the floor—What could be the:
  Cause?-leaking freezer
  Immediate cause?-door left open
  Root cause?-freezer not organized
    Items are not easily found
    Takes too long to find items
Root cause means digging deeper for an answer.
Why did this happen?
Cause (first response)
Ask “why” again..
Immediate cause (next response)
Ask “why” again..
Root cause (upon further thought)

## Slide 12: Start with a New Mindset
People are generally not the ultimate cause of problems
People implement processes
Most people do not come to work planning to sabotage their own work
Don’t waste time looking at surface issues
Use passive voice to avoid “blame game”
  Bob didn’t complete the form X correctly (WRONG)
  Form X lacks spaces for all the information
  Form X lacked necessary review and approval (CORRECT)

## Slide 13: One method of Root Cause Analysis: Cause Mapping (5 Whys)
Ask: “Why did this happen?” Write down the response, then ask the question again. Write down the response. Ask the question 5 - 6 times and you may get to the “root cause” of the problem. You may ask what and when questions, too:
Why was there water on the floor?
What could be the cause(s)?
Why would that happen?
When could that happen?

## Slide 14: Another method of Root Cause Analysis: Diagramming (Fishbone)
People (manpower)
  Training, verbal miscommunication, lack of communication, staff changed mid-project
Process/Methods
  Procedures, workflow,
  Measurement (Calibrations performed, but were they appropriate?)
Equipment (machines)
  Defective, not maintained, not calibrated, overloaded
Management
  Reviewed annually?
Environment
  Temperature, humidity, work area, distractions
Materials
  Incorrect, degradation, certificates of analysis

## Slide 15: Root Cause Analysis Corrective Action
Section 8.7.2
Once the root cause is identified, you must implement a fix (corrective action) to prevent it from happening again.
  Identify potential corrective actions
  Select and implement the action most likely to eliminate the problem and prevent recurrence
  Corrective actions are appropriate to the magnitude and risk of the problem

## Slide 16: Corrective Action
Once implemented, the laboratory monitors the results of the corrective action to ensure it was effective.
If effective, close the Corrective Action.
If not effective, select another Corrective Action or revisit the root cause.

## Slide 17: Corrective Action
Update any risks and opportunities determined during planning, if necessary
Make changes to the quality management system, if necessary

## Slide 18: Improvement
Section 8.6
Proactive process of continual improvement
Goal:
    Improvement of the quality management system
    Improvement of technical operations
    Elimination of potential nonconformities
System improvement stems from rigorously correcting problems and learning to foresee potential problems.

## Slide 19: Opportunities for Improvement
May be identified through the review of:
May be identified for laboratory documents, quality system, or laboratory processes
Operational procedures Use of the policies Overall objectives Audit results A result of normal work Observations Corrective actions | Analysis of data Proficiency tests Management review Suggestions from personnel Risk assessment Analysis of data

## Slide 20: Addressing Opportunities for Improvement
Develop an action plan
  Specify what situation needs improving
  Define what changes/actions need to occur
  Assign responsibility
  Implement necessary action
Monitor the action
  After implementation gather observations or data to determine whether the improvement action was effective.

## Slide 21: Seeking Feedback from Customers
Seek feedback, both positive and negative, from customers.
Analyze the feedback to improve:
  The quality management system
  Laboratory activities
  Customer service
Examples include customer surveys, records of communication, and review of reports with customers.

## Slide 22: Summing It Up
Quality management system SOPs define responsibilities and authorities for the root cause investigation process.
Root cause investigation is a problem-solving activity focused on the system, not the personnel.
Root cause investigation leads to corrective action, which is intended to prevent recurrence of nonconformance.
Improvement is a proactive process intended to prevent occurrence of nonconformance and improve the laboratory
Seek customer feedback for improvement areas.

## Slide 23: Reference
ISO/IEC 17025:2017 General requirements for the competence of testing and calibration laboratories
https://www.iso.org/standard/66912.html