## Slide 1: Module L4 Practical strategies for sequencing and molecular characterization of influenza viruses

## Slide 2: Considerations for Sequencing
What are my resources?
  Personnel
  Equipment
How many samples will my lab sequence?
  What kind of sequencer do / will I have?
    How many samples can it process simultaneously?
    What kind of read length does / will my sequencer produce?
  What kind of primer design strategy will I use?
    How much redundancy in my sequence do I want or need?
    What amplification and sequence strategy will I employ?
      Conventional
        Subtype / gene specific primers to amplify (~1000 bp amplicon)
        Different set of primers internally to sequence for each subtype and gene
      M13–labeled
        Subtype / gene specific primers to amplify (~500 bp amplicon)
        Only M13-forward and M13 reverse to sequence

## Slide 3: Considerations for Sequencing (cont.)
Do I have a specimen and data management system in place?
Need a solid method to identify the “uniqueness” of a specimen or isolate that is sequenced
Standard naming conventions need to be implemented when lab is set up
  Specimen names
  Amplifying and sequencing reactions
What type of pipeline will I use to analyze and report my sequencing results?
  Standardization is very important

## Slide 4: What and How Many Viruses/Genes do you Sequence?
Despite the increasing numbers of sequencers to choose from, sequencing is not cheap
  Need to choose the samples to sequence wisely
    Geographic location and temporal distribution
    Fatal or severe
    Antigenic variant
    Antiviral resistant
    Novel subtype in novel host
    Epidemiological study
How many depends on your research question
  New mutation – may want to see how widespread is the circulation
  New antigenic variant – may want to sequence a representative population to determine if there is molecular basis for the reactivity / emergence of new variant

## Slide 5: Determination of Sequencing Needs
What do you want to sequence
  Partial gene fragment for diagnosis?
  Whole gene
  Multiple genes
  Whole genome
Why do you want to sequence?
  Pathogen detection
  Mutation detection
  Understand the evolution of viruses
  Genetic basis of antigenicity and/or pathogenicity
  Comparison to vaccine strain

## Slide 6: High-throughput vs. Low-throughput
Resources
  Equipment
    Single channel vs. multichannel pipettes
    Manual versus robotic liquid handling
    Sequencer
      4 channel to 96 channel to NGS platforms
      How many sequencers available?
Throughput
  4 capillary ABI ~ 1 full genome / 40 hrs (3-5x coverage)
  96 capillary ABI ~ 12 full genomes / 24 hrs (3-5x coverage)
Financial Considerations
  Cost / reaction
  Some cost-savings through protocol modifications

## Slide 7: Data Management
Start-to-finish
  Specimen login – accessioning systems to track sample by number not by name
Take into account some metadata
  Specimen id#
    Most labs assign specimen number or code that makes that sample unique
      Can be as simple as a numerically increasing number and an Excel-style spreadsheet that records specimen number or code, date of specimen collection, patient age, patient gender, passage information for isolates, and possibly the extent of illness (recovered to fatal)
  Example
    Specimen ID = 2010216745
    Sample is a C1 Passage and we want to sequence the HA gene
      Example of an appropriate unique ID = 2010216745_C1_HA_v1
        This would be cross-referenced with the CDCID
        Could have additional versions of the same passage re-sequenced (i.e., _v2)
        Could have additional gene segments (i.e., _PB2, _PB1, _PA, etc…)
        Could have a different passage sequenced (i.e., _C2)

## Slide 8: First Generation Sequencing

## Slide 9: Sanger Sequencing
PCR reaction with chain termination and the ddNTPs are labeled
  Radioisotope
  Fluorescent
Amplified DNA is then separated according to size on gel electrophoresis
  Smallest to largest
  As fluorescent label passes through instrument laser beam, the kind of label is recorded in an electropherogram
Overlapping sequences are assembled into contigs
Notes: No citation for these images

## Slide 10: Sanger Methodology
Notes: Sanger Method Image http://www.the-scientist.com/?articles.view/articleNo/15939/title/DNA-Sequencing-Industry-Sets-its-Sights-on-the-Future/
Capillary Sequencing : https://jgi.doe.gov/archived-educator-resources/sanger-sequencing-archive/how-sanger-sequencing-is-done/step-10-capillary-sequencing/
No citation for these images

## Slide 11
Next Generation Sequencing (NGS)
Deep Sequencing & Next Generation Sequencing (NGS)
Properties of the Virus:
  Genomic variation
  Receptor binding
  Transmission in lab animals
  Antiviral Drug resistance
Influenza viruses exist as a quasi-species within a host
- NGS provides understanding of the frequency of mutations at a particular codon
Notes: Image PacBio RS II from Pacific Biosciences http://www.pacb.com/products-and-services/pacbio-systems/

## Slide 12: Sequence Variation
What factors impact variability?
Are the tools we have sufficient?
    Right tools / methods? Bioinformatics bias
    Instrument bias False negative and false positives
Notes: No citation for this image

## Slide 13: Mapping Mutations
Annotated reference
Known marker for mammalian adaptation, virulence etc.
http://www.cdc.gov/flu/avianflu/h5n1-genetic-changes.htm
Once desired depth of coverage is achieved, utilize variant detection software to detect mutations
Mutations detected may not be representative of the dominant population.
Mutations found may occur in residues that impact risk assessment.
Notes: No citation for this image

## Slide 14: Influenza Next Generation Sequencing (NGS) Efforts
Universal NGS sequencing
Unknown respiratory disease outbreak
Vaccine improvement
Outbreak response/ surveillance
Disease transmission
Disease detection
Notes: No citation for these images except:
Chickens and pig: Image purchased from Shutterstock. Stock photo ID: 116037238
Coughing person at bottom right: Image purchased from Shutterstock. Stock vector ID: 201932494

## Slide 15: The Instruments – Pros and Cons
PacBio RS
Long read length (8.5KB average) but high indel error high susceptibility to reference bias
Illumina MiSeq
Short read length, lowest error, generates the most sequence
Ion Torrent PGM
Short read length homopolymer error
Oxford Nanopore
MinION
Beta testing now
Long read length
Very high error rate
Notes: No citations for these images

## Slide 16: Which Tool is Best for Your Lab?
Wet lab process has to be tailored to the question
Considerations
  Error
  Input
  Outcome
  Cost
Notes: Image purchased from Shutterstock. Stock vector ID: 584901160

## Slide 17
Direct sequencing of PCR products (amplicons)
  Clinical materials
  Identification of quasi-species
  Identification of rare SNP patterns
  De Novo sequencing
  Longer reads all assembly of “shotgun” sequence data into a minimal number of contigs
  Whole Genome Sequences from different microbial genomes can be obtained with unprecedented throughput and speed
  Large-scale, parallel pyrosequencing
  Improved accuracy and read lengths (~ 400 bp)
Nature Biotechnology 26, 1117 - 1124 (2008) Published online: 9 October 2008
454 Sequencing
  Process
  Library prep – genomic DNA isolated, fragmented, and ligated to adapters and separated into single strands
  Emulsion PCR – fragments bound to beads (1 frag/bead)
  Emulsion is broken, DNA denatured, beads enriched and deposited in well of fiber-optic slide
  Small beads with pyroseq rxn deposited in each well
  Scanning em of empty wells
  454 instrument components consist of fluidic assembly (i) flow cell (ii) CCD Camera (iii)
Notes: No citations for these images.

## Slide 18: PacBio RS
Works by fixing DNA polymerase to wells on a plate
Laser detects sample through bottom of wells
Add ssDNA and fluorescently labeled nucleotides
Watch the bases being incorporated in real time
There is a limit to the read length
  The laser used for detection heats up the system and eventually burns out the polymerase
Notes: No citations for these images.

## Slide 19: Illumina MiSeq
Notes: No citations for these images.

## Slide 20: Ion Torrent PGM
Semiconductor sequencing
High density array of micro-machined wells that sense the release of H+ as part of base incorporation
  No lights, camera or action (scanning)
  Advantages
    Quick results
    Small footprint
    Low cost
  Still requires amplification of DNA template in each well and “wash-and-scan” methodology
    Limits read length (currently at 400 bp)
    Limits throughput
1-7-12 million sensors
Notes: No citations for these images.

## Slide 21: Oxford Nanopore Technology
Biological Nanopore construction
  Modified α-hemolysin pore
    exonuclease attached to extracellular face of the pore
  synthetic cyclodextrin sensor is covalently attached inside surface of the nanopore
  System wrapped in synthetic lipid bilayer
How it works
  DNA loaded onto exonuclease-containing face
  Voltage applied across bilayer by changing salt concentration
  Exonuclease cleaves off individual nucleotides
  Individual nucleotides detected
    Cleavage causes characteristic disruption of onic current through pore
Advantages
  Long read length
  High scalability
  Low cost (electronics vs optics)

## Slide 22: Typical Influenza Virus NGS Pipeline
Database
NGS library construction
RNA extraction
Universal
genomic amplification
Genome assembly and curation
Data integration and storage
Data Base
Next Generation Sequencing
Analysis
1
2
3
4
5
6
8
7
Inquiries regarding CDC’s sequencing SOPs and other questions can be directed to:
Dr. John Barnes (@cdc.gov); Dr. Todd Davis (eou8@cdc.gov)
Multiple vendors supply instruments/reagents/consumables for Sanger and NGS platforms
should be made in-country as there are cost differences depending on delivery location
Budget estimates should include purchasing annual warranties/service contracts for instrument preventative maintenance and repairs
Notes: No citations for these images.

## Slide 23: Molecular Characterization of influenza A(H7N9) Viruses

## Slide 24
0.01
R47M
R47K
R47K L217Q
A/Xuzhou/1/2013 H7N9
A/Wuxi/4/2013 H7N9
A/Nanjing/7/2013 H7N9
A/Nanjing/2/2013 H7N9
A/Zhenjiang/1/2013 H7N9
A/environment/Suzhou/14/2013 H7N9
A/Nanjing/4/2013 H7N9
A/environment/Zhenjiang/4/2013 H7N9
A/Environment/Guangdong/C13281025/2013 H7N9
A/Environment/Guangdong/C13281030/2013 H7N9
A/homing pigeon/Jiangsu/SD184/2013 H7N9
A/Taiwan/1/2013 H7N9
A/wild pigeon/Jiangsu/SD001/2013 H7N9
A/chicken/Zhejiang/DTID-ZJU01/2013 H7N9
A/environment/Henan/SD429/2013 H7N9
A/chicken/Shanghai/S1410/2013 H7N9
A/Shanghai/1/2013 H7N9
A/pigeon/Wenzhou/559/2013 H7N7
A/duck/Wenzhou/771/2013 H7N3
A/goose/Guangdong/7472/2012 H7N7
A/silkie chicken/Wenzhou/793/2013 H7N7
A/chicken/Wenzhou/690/2013 H7N7
A/chicken/Wenzhou/279/2013 H7N7
A/duck/Fujian/6380/2010 H7N3
A/duck/Fujian/6326/2010 H7N3
A/duck/Zhejiang/12/2011 H7N3
A/duck/Zhejiang/2/2011 H7N3
A/duck/Zhejiang/10/2011 H7N3
A/duck/Zhejiang/DK10/2013 H7N3
A/duck/Zhejiang/DK16/2013 H7N3
Phylogenetic Tree of H7 Hemagglutinin Gene
Q213P
R47K
T122A
L217I
A/chicken/Zhejiang/SD007/2013 H7N9
A/Anhui/1/2013 H7N9
A/chicken/Jiangsu/1021/2013 H7N9
A/Shanghai/2/2013 H7N9
A/Hangzhou/1/2013 H7N9
A/Zhejiang/1/2013 H7N9
A/Jiangsu/01/2013 H7N9
A/Suzhou/3/2013 H7N9
A/Zhejiang/22/2013 H7N9
A/Zhejiang/DTID-ZJU10/2013 H7N9
A/Guangdong/2/2013 H7N9
A/environment/Shenzhen/1/2013 H7N9
A/Guangdong/1/2013 H7N9
A/Hong Kong/5942/2013 H7N9
A/Nanjing/6/2013 H7N9
A/Wuxi/3/2013 H7N9
A/environment/Suzhou/8/2013 H7N9
A/Suzhou/5/2013 H7N9
L217Q
N267D
N282S
N190S
L217Q
L217Q
L217Q/L
A180T L217Q P230S D289E S304R
G119E L217Q
L217P S281N
V24G C54G L56P L57R I78M
L217Q
L217Q
A128S S165N V177G P212T L217Q N267D H274Y
V264I
S275G I317S
1st wave H7N9 viruses
2nd and 3rd wave H7N9 viruses
Amino acid changes compared to vaccine strains
Vaccine strains in red
Notes: No citations for this image.

## Slide 25
Glycosylation site at position 125 not present in Anhui/1/2013 HA
Equivalent to residue 226 in H3 numbering. Crucial for switching between α2-3 and α2-6 receptor specificity
Asian H7N9: orange
Netherlands: green
177
V or G
Points towards the RBS pocket; reduce α2-3 interactions
180
A or T
217
L or Q
125
A or T
Minimal impact on the RBS
Angela Yang/James Stevens
Receptor Binding Alteration Compared to Other Avian H7 Viruses
220-loop
130-loop
190-helix
150-loop

## Slide 26: A(H7N9) Receptor Binding Site (RBS) Mutations
RBS at positions 226 and 228 (H3 numbering) | 
98% of LPAI viruses from humans, birds and environment | 226L/228G (indicates decreased binding to alpha 2-3 receptors)
Less then 1% of LPAI viruses | 226Q/228G (H7 avian consensus); majority of HPAI H7N9 viruses are 226Q
Less than 1% of viruses | 226I/228G (point mutation change to isoleucine)
Less than 1% of viruses | 226P/228G (point mutation to proline)

## Slide 27
Notes: No citations for these images.

## Slide 28
A/Jiangsu/2/2013_H7N9
A/Jiangsu/1/2013_H7N9
A/Nanjing/1/2013_H7N9
A/Nanjing/2/2013_H7N9
A/Zhenjiang/1/2013_H7N9
A/Zhejiang/2/2013_H7N9
A/Zhejiang/DTID-ZJU01/2013_H7N9
A/Zhejiang/20/2013_H7N9
A/environment/Suzhou/8/2013_H7N9
A/Changsha/2/2013_H7N9
A/Changsha/1/2013_H7N9
A/Taiwan/T02081/2013_H7N9
A/Taiwan/1/2013_H7N9
A/Shanghai/2/2013_H7N9
A/Anhui/1/2013_H7N9
A/Suzhou/3/2013_H7N9
A/Nanjing/6/2013_H7N9
A/Xuzhou/1/2013_H7N9
A/Nanjing/7/2013_H7N9
A/Suzhou/5/2013_H7N9
A/Nanjing/4/2013_H7N9
A/Wuxi/4/2013_H7N9
A/Shanghai/1/2013_H7N9
A/brambling/Beijing/16/2012_H9N2
A/environment/Suzhou/14/2013_H7N9
A/Zhejiang/22/2013_H7N9
A/Zhejiang/DTID-ZJU05/2013_H7N9
A/chicken/Shanghai/C1/2012_H9N2
A/chicken/Zhejiang/329/2011_H9N2
A/environment/Zhenjiang/4/2013_H7N9
A/chicken/Zhejiang/Q1D4/2010_H9N2
A/chicken/Shanghai/C2/2012_H9N2
A/chicken/Shanghai/C3/2012_H9N2
A/chicken/Jiangsu/Q3/2010_H9N2
A/chicken/Zhejiang/607/2011_H9N2
A/chicken/Wuxi/7/2010_H9N2
A/chicken/Anhui/HF/2010_H9N2
A/chicken/Tongshan/1/2011_H9N2
A/chicken/Jiawang/2/2011_H9N2
A/chicken/Yongcheng/1/2011_H9N2
A/chicken/Qianzhou/12/2010_H9N2
A/chicken/Shandong/03/2010_H9N2
A/chicken/Shandong/H/2009_H9N2
A/chicken/Shandong/02/2010_H9N2
A/chicken/Shandong/BD/2010_H9N2
A/chicken/Guangdong/ZHJ/2011_H9N2
A/chicken/Guangdong/ZCY/2011_H9N2
A/Hong Kong/5942/2013_H7N9
A/Guangdong/1/2013_H7N9
A/Guangdong/02/2013_H7N9
A/chicken/Vietnam/NCVD-1156/2011_H9N2
A/canine/Guangxi/1/2011_H9N2
A/equine/Guangxi/3/2011_H9N2
PB2
A/Zhejiang/22/2013_H7N9
A/Zhejiang/DTID-ZJU05/2013_H7N9
A/Anhui/1/2013_H7N9
A/chicken/Shanghai/S1076/2013_H7N9
A/environment/Suzhou/14/2013_H7N9
A/Zhejiang/DTID-ZJU01/2013_H7N9
A/Wuxi/3/2013_H7N9
A/environment/Suzhou/8/2013_H7N9
A/Xuzhou/1/2013_H7N9
A/Wuxi/2/2013_H7N9
A/chicken/Zhejiang/SD033/2013_H7N9
A/Nanjing/4/2013_H7N9
A/environment/Zhenjiang/4/2013_H7N9
A/Shanghai/2/2013_H7N9
A/Taiwan/1/2013_H7N9
A/Zhejiang/1/2013_H7N9
A/Shanghai/1/2013_H7N9
A/chicken/Zhejiang/SD007/2013_H7N9
A/chicken/Dawang/1/2011_H9N2
A/chicken/Shuanggou/1/2011_H9N2
A/chicken/Xigou/1/2011_H9N2
A/environment/Shanghai/S1436/2013_H7N9
A/brambling/Beijing/16/2012_H9N2
A/chicken/Vietnam/OIE-1611/2012_H9N2
A/environment/Shanghai/S1438/2013_H7N9
A/environment/Shanghai/S1437/2013_H7N9
A/chicken/Taixing/10/2010_H9N2
A/chicken/Yangzhou/11/2010_H9N2
A/chicken/Shandong/1231/2008_H9N2
A/chicken/Shandong/SG2/2009_H9N2
A/chicken/Tibet/S1/2009_H9N2
A/chicken/Tibet/S4/2009_H9N2
A/chicken/China/AH-10-01/2010_H9N2
A/chicken/Shandong/01/2010_H9N2
A/chicken/Shandong/02/2009_H9N2
A/environment/Xinjiang/6/2009_H5N1
A/chicken/Shandong/12/2008_H9N2
A/environment/Chang Sha/6/2009_H9N2
A/chicken/Zhejiang/HJ/2007_H9N2
A/chicken/Shandong/HY/2009_H9N2
A/chicken/Shandong/KD/2009_H9N2
A/chicken/Hubei/10/2009_H9N2
A/chicken/Hunan/6108/2005_H9N2
A/chicken/Hunan/4444/2005_H9N2
A/chicken/Hunan/5260/2005_H9N2
A/chicken/Hebei/0329/2007_H9N2
A/chicken/Shandong/LY/2006_H9N2
A/chicken/Shanghai/1/2002_H9N2
A/chicken/Shanghai/2/2002_H9N2
A/duck/Zhejiang/3/2002_H9N2
A/chicken/Henan/1/2004_H9N2
A/Hong Kong/5942/2013_H7N9
A/Guangdong/1/2013_H7N9
A/Guangdong/02/2013_H7N9
A/swine/Taizhou/5/2008_H9N2
A/chicken/Vietnam/NCVD-1156/2011_H9N2
A/chicken/Jiangsu/Q3/2010_H9N2
NS
Genetic diversity among H7N9 viruses found in internal genes
Internal genes derived from avian influenza A(H9N2) viruses circulating in China
At least 9 unique genotypes detected in China in first 2 waves (multiple reassortment events prior to or after emergence)
Viruses from southern China have somewhat different genotype from northern China
H7N9 virus is well-distributed across several regions of China
Notes: No citations for these images.

## Slide 29
Molecular-based surveillance of A(H7N9) viruses indicated stability of mutations associated with mammalian adaptation, transmission, virulence and susceptibility to antiviral drugs
Gene | Mutation(s) | Phenotype | H7N9 viruses
NA | R292K | Marker of decreased susceptibility to neuraminidase inhibitors | ~10% of human viruses in the 5th wave
PB2 | 89V E627K D701N | Increased virulence in mice Increased virulence in mice Mammalian host adaptation, increased virulence and transmission | All viruses Few human viruses have 627E, all avian/environmental are 627E Multiple human viruses have 701N
PB1 | H99Y/I368V | H5 virus transmissible among ferrets | All viruses 99H; majority have 368V
M1 | N30D/T215A | Increased virulence in mice | All viruses
M2 | S31N | Decreased susceptibility to adamantane drugs | All viruses
NS | P42S PDZ ligand | Increased virulence in mice Increased virulence in mice | All viruses All viruses are truncated

## Slide 30
M227L A292T
N190S
G276R
M256I
M227I
S118N R130K R303K
T122I M256I
S118N
A266D
S127G
G261E
R130K
S118N R130K V264I I317V
S118N R130K
I120T
R130K
R130K
R130K
R130K
R130K
S118N
A112T M227I
D109E P206L
N17D A266V
N37S S290R
I101V R130K N282S
R130K S134P
N267D
D246E
V49I I280T
V177A
N267D
S118N R130K
A112S
S118N
I258V
V49I
S118N I288V
S118N
S118N
R47K
R47K N267D
E104K
L168I
R47K
N282S
R47K
R47K R303K
Q213P
V24G
T122A
R47K T122A
N190S
R47M
R47K L217Q
A125V
L168I
A/Shanghai/1/2013 H7N9
A/Shanghai/JS01/2013 H7N9
A/pigeon/Wuxi/0405007G/2013 H7N9
A/chicken/Shanghai/S1410/2013 H7N9
A/chicken/Zhejiang/C481/2013 H7N9
A/chicken/Guangzhou/1/2013 H7N9
A/wild pigeon/Jiangsu/SD001/2013 H7N9
A/Guangdong/03/2013 H7N9
A/chicken/Shenzhen/712/2013 mixed
A/Hong Kong/734/2014 H7N9
A/Hong Kong/5942/2013 H7N9
A/Hong Kong/470129/2013 H7N9
A/Guangdong/1/2013 H7N9
A/Shenzhen/SP-W1/2014
A/Guangzhou/1/2014 H7N9
A/Hong Kong/8113530/2014 H7N9
A/environment/Guangzhou/XN07390/2014 H7N9
A/environment/Guangzhou/XN12917/2014 H7N9
A/silkie chicken/Shantou/1406/2014
A/chicken/Shenzhen/138/2014
A/silkie chicken/Dongguan/1264/2014
A/Hong Kong/2212982/2014 H7N9
A/Hong Kong/3263/2014 H7N9
A/Hong Kong/5731/2014 H7N9
A/Guangdong/15SF010/2015 H7N9 *
A/Duck/Guangdong/DG527/2014 H7N9
A/Chicken/Guangdong/DG592/2014 H7N9
A/Hong Kong/8130773/2015 H7N9 *
A/Hong Kong/2550/2015 H7N9 *
A/Guangdong/02496/2014 H7N9
A/Environment/Guangdong/DG127/2015 H7N9 *
A/Duck/Guangdong/DG103/2015 H7N9 *
A/Hong Kong/8194273/2014 H7N9
A/Hong Kong/4495/2014 H7N9
A/chicken/Dongguan/1100/2014 mixed
A/Hong Kong/5581/2014 H7N9
A/chicken/Guangdong/G1381/2014 H7N9
A/Hong Kong/8122430/2014 H7N9
A/chicken/Shantou/1550/2014
A/Hong Kong/VB16049808/2016 H7N9 *
A/Guangdong/60923/2016 H7N9 *
A/Hong Kong/61/2016 H7N9 *
A/Hong Kong/214/2017 H7N9
A/silkie chicken/Huzhou/4213/2013
A/Huai'an/083/2014 H7N9
A/chicken/Shanghai/PD-CN-02/2014
A/chicken/Zhangzhou/8585/2014
A/duck/Wenzhou/RAQL10/2015 H7N9 *
A/Zhejiang/1/2016 H7N9 *
A/Zhejiang/LS01/2014 H7N9
A/silkie chicken/Jiangxi/9469/2014
A/chicken/Jilin/SD020/2014 H7N2
A/Jiangsu/98342/2014 H7N9
A/Zhejiang/22/2013 H7N9
A/Zhejiang/DTID-ZJU10/2013 H7N9
A/Anhui/1/2013 H7N9
A/Wuxi/1/2013 H7N9
A/Shanghai/2/2013 H7N9
A/chicken/Guangdong/SD641/2013 H7N9
A/Beijing/1/2013 H7N9
A/Changsha/1/2013 H7N9
A/Shanghai/07/2013 H7N9
A/Zhejiang/DTID-ZJU08/2013 H7N9
A/Zhejiang/DTID-ZJU05/2013 H7N9
A/Huzhou/1/2013 H7N9
A/Wuxi/3/2013 H7N9
A/Nanjing/7/2013 H7N9
A/Huzhou/10/2013 H7N9
A/Nanjing/6/2013 H7N9
A/Suzhou/5/2013 H7N9
A/Xuzhou/1/2013 H7N9
A/chicken/Jiangsu/S002/2013 H7N9
A/Zhejiang/DTID-ZJU02/2013 H7N9
A/Zhejiang/HZ1/2013 H7N9
A/Zhenjiang/1/2013 H7N9
A/Taiwan/T02081/2013 H7N9
A/pigeon/Zhejiang/P2/2013 H7N9
A/Taiwan/1/2013 H7N9
A/Shanghai/5190T/2013 H7N9
A/Taiwan/3/2013 H7N9
A/Shanghai/01/2014 H7N9
A/Shanghai/Mix1/2014 H7N9
A/Shanghai/PD-01/2014
A/Huzhou/5/2013 H7N9
A/duck/Jiangxi/15044/2014
A/Taiwan/1/2014 H7N9
A/Taiwan/2/2014 H7N9
A/goose/Jiangsu/J1111/2014 H7N9
A/Fujian/5/2015 H7N9
A/Fujian/18/2015 H7N9 *
A/British Columbia/1/2015 H7N9 *
A/Fujian/27/2015 H7N9
A/chicken/China/028/2014 H7N9
A/Huai'an/001/2015 H7N9 *
A/duck/Anhui/A1618/2014 H7N9
A/Xinjiang/05845/2015 H7N9 *
A/Xinjiang/98692/2014 H7N9
A/chicken/Anhui/A1065/2014 H7N9
A/Jiangsu/19758/2015 H7N9 *
A/Environment/Hunan/10086/2016 H7N9 *
A/Environment/Hunan/10125/2015 H7N9 *
A/Hunan/06197/2016 H7N9 *
A/chicken/Wenzhou/HATSLG01/2015 H7N9 *
A/Fujian/1/2016 H7N9 *
A/Fujian/06198/2016 H7N9 *
A/Fujian/10/2015 H7N9 *
A/Shantou/2004/2015 H7N9
A/Chicken/Guangdong/SW154/2015 H7N9 *
A/Fujian/09273/2015 H7N9 *
A/Guizhou/03240/2015 H7N9 *
A/Environment/Guangdong/15123/2016 H7N9 *
A/Environment/Guangdong/15120/2016 H7N9 *
A/Guangdong/MZ828/2015 H7N9 *
A/Quzhou/1/2015 H7N9 *
A/duck/Wenzhou/YJYF24/2015 H7N9 *
A/Beijing/40610/2015 H7N9 *
A/Anhui/40094/2015 H7N9
A/Anhui/26836/2016 H7N9 *
A/Anhui/26837/2016 H7N9 *
A/Jiangsu/15028/2016 H7N9 *
A/Zhejiang/15/2016 H7N9 *
A/Jiangsu/03756/2016 H7N9 *
A/Environment/Jiangsu/03758/2015 H7N9 *
A/Jiangsu/06307/2014 H7N9
A/Jiangsu/03753/2016 H7N9 *
A/duck/Jiangsu/J3619/2014 H7N9
A/Hebei/46587/2016 H7N9 *
A/Zhejiang/12/2016 H7N9 *
A/Hunan/02286/2017 H7N9
A/Jiangsu/60456/2016 H7N9 *
A/Jiangsu/60460/2016 H7N9 *
A/Jiangsu/60454/2016 H7N9 *
A/Fujian/8/2016 H7N9 *
A/Fujian/30767/2016 H7N9 *
A/Environment/Guangdong/15125/2016 H7N9 *
A/Guangdong/15SF871/2015 H7N9 *
A/Anhui/26835/2016 H7N9 *
A/Hunan/06196/2016 H7N9 *
A/Fujian/3/2016 H7N9 *
A/Guangdong/16SF007/2016 H7N9 *
A/Hunan/04135/2016 H7N9 *
A/Hunan/04137/2016 H7N9 *
A/Tianjin/43917/2016 H7N9 *
A/Jiangsu/05155/2016 H7N9 *
A/Liaoning/44068/2016 H7N9 *
A/Jiangsu/15027/2016 H7N9 *
A/Fujian/5/2016 H7N9 *
A/Fujian/45970/2016 H7N9 *
A/Fujian/54840/2016 H7N9 *
A/Fujian/17527/2016 H7N9 *
A/Fujian/4/2016 H7N9 *
A/Hunan/02650/2016 H7N9 *
A/Fujian/30766/2016 H7N9 *
A/Anhui/45322/2016 H7N9 *
A/Hong Kong/793/2016 H7N9 *
A/Jiangsu/15026/2016 H7N9 *
A/Environment/Hebei/40052/2016 H7N9 *
A/Environment/Hebei/40049/2016 H7N9 *
A/Environment/Hebei/40053/2016 H7N9 *
A/Hebei/38604/2016 H7N9 *
A/Beijing/44066/2016 H7N9 *
A/Beijing/39450/2016 H7N9 *
A/Hubei/39269/2016 H7N9 *
A/Hong Kong/4553/2016 H7N9 *
A/Hong Kong/125/2017 H7N9
A/Environment/Guangdong/43966/2016 H7N9 *
A/Anhui/60926/2016 H7N9 *
A/Anhui/60934/2016 H7N9 *
A/Anhui/60935/2016 H7N9 *
A/Anhui/60933/2016 H7N9 *
A/Anhui/60932/2016 H7N9 *
A/Anhui/60931/2016 H7N9 *
A/Hong Kong/VB16064646/2016 H7N9 *
A/Zhejiang/9/2016 H7N9 *
A/Jiangsu/60450/2016 H7N9 *
A/Zhejiang/10/2016 H7N9 *
A/Zhejiang/16/2016 H7N9 *
A/Jiangsu/60447/2016 H7N9 *
A/Zhejiang/14/2016 H7N9 *
A/Zhejiang/11/2016 H7N9 *
A/Jiangsu/60458/2016 H7N9 *
A/Jiangsu/60457/2016 H7N9 *
A/Jiangsu/60459/2016 H7N9 *
A/Hunan/02285/2017 H7N9
A/Zhejiang/13/2016 H7N9 *
A/Anhui/60936/2016 H7N9 *
A/Fujian/02152/2017 H7N9
A/Jiangsu/60451/2016 H7N9 *
A/Zhejiang/6/2016 H7N9 *
A/Jiangsu/60466/2016 H7N9 *
0.0025
A128S S165N V177G P212T L217Q N267D H274Y
S165N V177G V205A P212T L217Q N267D
G119E L217Q
L217Q
T116K
V86I R130K N282S
N267D
V49I
V264I N267G
I108L S134P Q213P G216A M227I S237N M256I N267D
I280M
E25V T194I S207I
A210E
N37S
R47K I78V V262A N282K
A74T S275N
A9S
E104K
E104R T156N T179I
E104K N282K
E104K
K2R R130K Q154H
E104G V177A S237N D246V
T36K D109E z
A125T
A125V
L168I S290N zzz
I38F L57R
L57R
R47K
S127G R211G
L217Q
L217P S281N
R252K
P206S E269K
S304G
R346K/R
G216D
K184N
S118N
I108L S218F I258V D289N
E269V
R103K M256I D271I
G133E
G23E K319R
V86F
D367Y/D
S218F M227I
M256I I280V
P212Q/P
T59I
I38V A112T
R130N
K184N/K
K184N/K
K184N
A128V/A
T59A
R130M
R130K
R130M N267Y
R130K N282S
R130K
R130K
R130K
S281N/S
R298K
D271N
P208T
G261R/G D271G
S127N/S
V214F
I120T
L217I
T126A/T V262A
V170I
Feb-2013
Mar-2013
Apr-2013
May-2013
Jul-2013
Aug-2013
Oct-2013
Nov-2013
Dec-2013
Jan-2014
Feb-2014
Mar-2014
Apr-2014
May-2014
Jun-2014
Nov-2014
Dec-2014
Jan-2015
Feb-2015
Apr-2015
Dec-2015
Jan-2016
Feb-2016
Mar-2016
Apr-2016
May-2016
Jun-2016
Jul-2016
Oct-2016
Nov-2016
Dec-2016
Jan-2017
Evolution of Influenza A(H7) HA, China
Reassortant vaccine candidate in red
CDC HI reference viruses in blue
Viruses analyzed by CDC
5th epidemic H7N9 viruses
Tree branches of human viruses are in red (─)
Amino acid differences shown are relative to A/Shanghai/2/2013
Eastern China / Yangtze River Delta lineage
Southern China / Pearl River Delta lineage
Notes: No citations for this image.

## Slide 31
WHO Global Influenza Surveillance and Response System (GISRS) Surveillance and Vaccine Development

## Slide 32: Global Influenza Surveillance Network
Disease surveillance: Determine the extent and severity of epidemics / pandemics
  networks of sentinel physicians
  mortality due to pneumonia and influenza (P&I)
Virologic surveillance: Determine antigenic and genetic properties of viruses that are circulating
  antigenic analysis using HAI, neutralization tests
  sequence analysis of HA, NA / full genomes
  screening for resistance to amantadine / rimantadine and neuraminidase inhibitors
  Create diagnostic tools for circulating viruses

## Slide 33: WHO Vaccine Recommendations
Northern Hemisphere Season: November – April
WHO Vaccine Recommendation: February
Southern Hemisphere Season: April – September
WHO Vaccine Recommendation: September
Atlanta
Memphis
London
Beijing
Tokyo
Melbourne
Notes: No citations for this image

## Slide 34: Considerations for New Vaccine Strain Recommendations
Are there new antigenic variants?
  Antigenic and genetic characterization
Are new variants spreading?
  Influenza activity and isolation of variants
Are current vaccines able to induce antibodies to the new variants?
  Serological evaluation of vaccinated individuals
Are any new variants useful for vaccine production?
  Egg isolate
  High growth in egg reassortants

## Slide 35: Vaccine Strain Selection: Time Line
Note: FDA is the U.S. Food and Drug Administration
Notes: No citations for these images, which are all grouped.

## Slide 36
Egg-Based Production Time
0
80
160
240
320
400
480
560
640
720
800
40
42
44
46
48
50
52
2
4
6
8
10
12
14
16
18
20
0
2
4
6
8
10
12
14
16
18
20
A(H3)
A(H1)
A(Unsubtyped)
B
Week
Number of Isolates
Percent Positive
Vaccine production
Respiratory Specimens Positive for Influenza, USA
Notes: No citations for these images.

## Slide 37
0
500
1000
1500
2000
2500
40
42
44
46
48
50
52
2
4
6
8
10
12
14
16
18
20
Week
Number of Isolates
0
4
8
12
16
20
24
28
32
36
40
Percent Positive
A(H3)
A(H1)
A(Unsubtyped)
B
Northern Hemisphere Season
Respiratory Specimens Positive for Influenza, USA
Notes: No citations for these images.

## Slide 38
A
B
C
D
E
Nucleotide changes can be silent (synonymous) or result in an amino acid change (non-synonymous)
If the amino acid change is in an antigenic site (regions where antibodies bind) of a surface protein (HA and/or NA) then antigenic drift can occur
Antigenic drift: antibodies to the previous strain no longer recognize new strain
A new vaccine is needed!
When Genetic Drift Leads to Antigenic Drift
Notes: No citations for this image

## Slide 39
A(H7N9) 5th wave hemagglutinin changes compared to A/Shanghai/2/2013 (candidate vaccine virus)
Pearl River Delta lineage
180° rotation
Yangtze River Delta lineage
N282K
D340N
N267D
M227I
E104K
R130K
A125V
E378A
S485R
A112T
S118N
180° rotation
Not visible
V425I
L168I
M227I
L168I
Site A - green
Site B - brownish
Site C - dark blue
Site D - cyan
Site E - yellow
CHO – orange
HA2 changes in red
Notes: No citations for these images.

## Slide 40
0.005
A/chicken/Wenzhou/WZTSLG02/2015
A/Guangdong/0012/2014
A/Hunan/02650/2016
A/Jiangsu/03753/2016
A/Guangdong/60060/2016
A/chicken/Fujian/11766/2016
A/British_Columbia/1/2015
A/Fujian/30767/2016
A/Guangdong/60061/2016
A/chicken/Wenzhou/201/2014
A/Jiangsu/15028/2016
A/Anhui/02/2013
A/Jiangsu/18828/2014
A/chicken/Guangzhou/4954/2016
A/Shenzhen/SP195/2015
A/Shanghai/1/2013
A/Hong Kong/5942/2013
A/Fujian/1/2016
A/Environment/Jiangsu/03137/2013
A/ZJ/22/2013
A/ZJ/DTID-ZJU05/2013
A/chicken/Fujian/11089/2016
A/Jiangsu/15027/2016
A/Taiwan/1/2017
A/Guangdong/SP38/2014
A/Beijing/01-A/2013
A/Guangdong/60923/2016
A/Hubei/39269/2016
A/Jiangsu/60466/2016
A/Anhui/45322/2016
A/chicken/GD/874/2014
A/Shandong/01/2014
A/chicken/Shaoxing/5201/2013
A/Jiangsu/06463/2017
A/Zhejiang/1/2016
A/Hebei/38604/2016
A/Fujian/45970/2016
A/Hong Kong/VB16049808/2016
A/Shanghai/14/2013
A/Shanghai/2/2013
A/Jiangsu/09387/2014
A/Xinjiang/05916/2014
A/Hunan/06196/2016
A/Anhui/60936/2016
A/Hunan/06948/2017
A/chicken/Jiangxi/14879/2015
A/shanghai/05/2013
A/Jiangsu/06454/2017
A/chicken/Guangzhou/1083/2016
A/Hunan/02287/2017
A/Fujian/02152/2017
A/chicken/Wuxi/SC4315/2015
A/Hong Kong/125/2017
A/Hong Kong/VB16189623/2016
A/Anhui/60933/2016
A/Fujian/15/2014
A/Hebei/46586/2016
A/Hong Kong/214/2017
A/Taiwan/1/2014
A/chicken/Jiangxi/18482/2014
A/Guangdong/17SF004/2017
A/Hong Kong/8130773/2015
A/Jiangsu/15026/2016
A/Hunan/04137/2016
A/Tianjin/43917/2016
A/Beijing/44066/2016
A/Fujian/54840/2016
A/Environment/Guangdong/C16283222/2016
A/Huaian/065/2014
A/Jiangsu/60460/2016
A/Guangdong/17SF003/2016
A/silkie chicken/Shantou/9473/2016
A/Hong Kong/4553/2016
A/Guangdong/17SF006/2017
A/Taiwan/2/2014
A/Anhui/1/2013
A/Liaoning/44068/2016
A/Guangdong-Guangzhou/XN08763/2014
A/Zhejiang/17/2014_W2-4
A/Fujian/18/2015
A/Guangzhou/1/2014
Yangtze River Delta
Pearl River Delta
93
85
76
88
70
87
83
88
86
71
98
89
93
98
87
100
100
100
95
P
E
I
P
K
G
-
-
-
R
G
P
E
V
P
K
R
K
R
T
A
R
G
-
Notes: No citations for these images.

## Slide 41: Genetic changes Identified in HPAI A(H7N9) Viruses
R163K
G261R
K130R
L217Q
I38T
180° rotation
Not visible:
I317V
V425I
A/Guangdong/17SF003/2016 HPAI
Cleavage site has polybasic insertion (KRTA)
K164E
T112P
E389K
Notes: No citations for this image

## Slide 42: A(H7N9) Antigenic Cartography
Serum raised to current CVVs
Antigens
Antigenic relationships of current and previous A(H7N9) viruses performed by CDC
Antigenic analysis indicated some viruses from Eastern China lineage have reduced cross-reactivity with existing candidate vaccine viruses
Pearl River delta lineage isolates
Notes: No citation for this image

## Slide 43: A(H7N9) Antigenic Cartography
Serum raised to current CVVs
Antigens
Antigenic relationships of current and previous A(H7N9) viruses performed by CDC
Antigenic analysis indicated some viruses from Eastern China lineage have reduced cross-reactivity with existing candidate vaccine viruses
Yangtze River delta lineage isolates
Notes:   Anhui/1 wt virus and Anhui/1 RG33A CVV were 4-fold down comparing homologous to heterologous titers
  Shanghai/2 wt virus were 4 to 8-fold down
  Shanghai/2 CVV RG32A virus were 4 to 8-fold down
  Both Anhui/1 and Shanghai/2 wt and CVVs were 2-fold down or equivalent comparing homologous to heterologous titers
  No citation for this image

## Slide 44: A(H7N9) Antigenic Cartography
Serum raised to current CVVs
Antigens
Antigenic relationships of HPAI A(H7N9) viruses performed by CDC
Antigenic analysis indicated have reduced cross-reactivity with existing candidate vaccine viruses
HPAI A(H7N9) isolates
Notes:   Anhui/1 wt virus and Anhui/1 RG33A CVV were 4-fold down comparing homologous to heterologous titers
  Shanghai/2 wt virus were 4 to 8-fold down
  Shanghai/2 CVV RG32A virus were 4 to 8-fold down
  Both Anhui/1 and Shanghai/2 wt and CVVs were 2-fold down or equivalent comparing homologous to heterologous titers
  No citation for this image

## Slide 45: Engineering Candidate Vaccine Viruses (CVVs) for A(H7N9)
CDC
A/Hong Kong/125/2017 RG56B
AS-C
AS-B
AS-A
AS-D
AS-E
CHO
R163K
G261R
K130R
L217Q
I38T
180° rotation
Not visible:
I317V
V425I
A/Guangdong/17SF003/2016 HPAI
Development by NIBSC, UK and China CDC
Cleavage site has polybasic insertion (KRTA)
K164E
T112P
E389K
CDC
A/Hong Kong/125/2017 +
RG56N
K130R
L217Q
K164E
T112P
HPAI-like (4 substitutions)
AS – Antigenic Site
CHO – Carbohydrate
WHO-VCM HPAI Recommendation
David Wentworth, Vivien Dugan et al.

## Slide 46: WHO Website for Vaccine Recommendations
http://www.who.int/influenza/vaccines/virus/recommendations/en/

## Slide 47: The findings and conclusions in this presentation are those of the authors and do not necessarily represent the official position of the Centers for Disease Control and Prevention.
Questions?